Name:_____________________

GIS in Water Resources

Homework#1

1.  The way that data is represented within a geographic information system enables the analysis that can be performed.  Discuss, based upon the lectures to date and your reading of Arc Hydro pages 1-31 and the ArcGIS and Spatial Analyst handouts, how the data representations you have learned about enable useful analyses.  Please limit your writing to no more than 300 words."

2.  The map below shows Utah and the display parameters of the State Plane coordinate system for the Utah Central Zone.

(a)  Sketch on the map the standard parallels, the central meridian and the latitude of origin of this projection.

(b)  For this projection, the coordinates of the origin (o, o) =

and the corresponding (Xo, Yo) =

(c)  What earth datum is used in this coordinate system?

(d)   What map projection is used in this coordinate system?

3.  Following are the geographic coordinates of the 3 cities involved in this class.

| City | Latitude | Longitude |
| --- | --- | --- |
| Logan | 41.7355 | -111.8344 |
| Lincoln | 40.8000 | -96.6670 |
| Austin | 30.2671 | -97.7431 |

a)  Calculate the great circle "curved earth" distance between each combination of cities (i.e. Logan to Austin, Austin to Lincoln and Lincoln to Logan).  Assume a spherical earth with radius 6370 km.

b)  Use ArcGIS to display these cities using the USA Contiguous Equidistant Conic projection.  For this projection report the following parameters:

Central_Meridian:

Standard_Parallel_1:

Standard_Parallel_2:

Latitude_Of_Origin:

c)  Calculate the X and Y coordinates of each city using the USA Contiguous Equidistant Conic projection.  Report your results in a table.

d)  Calculate the distance between each combination of cities from the USA Contiguous Equidistant Conic projection X and Y coordinates.