## Slide 1
Onion creek catchment modeling using PIHM
By,
Harish Sangireddy
PhD Candidate
The University of Texas at Austin

## Slide 2: What is PIHM?
Penn State Integrated Hydrologic Modeling system
It is a distributed hydrologic model that incorporates
  Channel routing
  Surface overland flow
  Subsurface flow
  Snow melt
  Evapotranspiration
via a semi-discrete approach with FVM.

## Slide 3: Procedural framework of PIHM
Raster processing
Vector processing
TIN generation ( domain decomposition)
Data model loader
  mesh, att, riv, para, soil, geol, LC, Init, calib, Forc
Run PIHM
Information visualization
  Temporal
  Spatial

## Slide 4: Outputs from PIHM
Time series plots
Spatial plots
Inflow, Outflow, Base flow, Surface flow
Saturated state, unsaturated state
Evaporation from Canopy
Transpiration, and Infiltration

## Slide 5: Onion Creek
Catchment Attributes | Catchment attribute values
HUC_8 | 12090205
HUC_10 | 1209020504
HUC_12 | 120902050407
HUC_10_Name | Onion creek – Colorado River
HUC_12_Name | Slaughter creek – onion creek
Catchment area in square meters | 238860.9755
Travis County

## Slide 6: Onion creek
30 m DEM used
After pit filling was performed, an area threshold of 7588 m^2 was suggested by PIHM to create stream lines
Subsequently the vector processing was done and the TIN was generated for the entire Onion creek.
The forcing data for this experiment is from 2005 - 2009

## Slide 7: Onion creek
30 m DEM used
After pit filling was performed, an area threshold of 7588 m^2 was suggested by PIHM to create stream lines
Subsequently the vector processing was done and the TIN was generated for the entire Onion creek.
Geology

## Slide 8: Onion creek
30 m DEM used
After pit filling was performed, an area threshold of 7588 m^2 was suggested by PIHM to create stream lines
Subsequently the vector processing was done and the TIN was generated for the entire Onion creek.
Land cover

## Slide 9: Onion creek
30 m DEM used
After pit filling was performed, an area threshold of 7588 m^2 was suggested by PIHM to create stream lines
Subsequently the vector processing was done and the TIN was generated for the entire Onion creek.
Soil type

## Slide 10: Model settings
Uniform climate conditions used
The soil, geology, land cover of HUC 12 was used

## Slide 11: Model settings
Initial conditions were set to zero

## Slide 12: Time series visualization from PIHM outputs
Diurnal signal
Simulated over a 7 day period
Uniform distribution of climate variables assumed.

## Slide 13: Spatial data visualization
Unsaturated zone head
Evapotranspiration
Correlates well with the land cover

## Slide 14: Saturate zones mapped with warning zones
Good spatial correlation between saturated zones identified by the PIHM model, and the warning zones from FEMA, even when the soil and geology characteristics are not accurate representation of the region.

## Slide 15: Caveats of this experiment
In order to run PIHM, the soil characteristics requires a compilation of the silt %, sand %, and clay % of each soil type in the HUC12.
Similarly the geology input file for PIHM needs information about the hydraulic conductivity, porosity, Van Genuchten soil parameters and some more.
The data preprocessor shipped with PIHM source code does not convert the raw data to data format as required the PIHM correctly always for soil and geology type.
Hence the first few runs of the PIHM model failed.
Although the soil and geology data was available for this region, the results that I present do not accurately represent the soil and geology characteristics of the onion creek. I was only able to find the silt %, sand %, and clay % of a few mukey ids only.

## Slide 16: Conclusions and Future work
I am going to use the SSURGO tables chorizon to get the real estimates of silt, clay and sand percentages for each mukey and re-run the PIHM model again.
I adjusted the shell scripts for PIHM to make it run on windows machine.
The preprocessor to PIHM cannot handle large time series as it runs out of memory. Hence simulations using more than 4 years of forcing data are difficult to run now.
By changing the soil and geology parameters, we can get better estimates of outflow.
Also the vector processing needs some manual intervention to make the TIN appropriately.