## Slide 1
An Approach to Sizing a
Rainwater Cistern
by
Russell B. Thomas
17 November 2011

## Slide 2: Agenda
Motivation for Project
Methodology
The Move to Colorado
Limitations
Questions

## Slide 3
Motivation: Water Independence from above!!
http://www.ulrichlogcabins.com/log-cabins/texas-log-cabin.php?Rocky-Ridge-Series-4
Scenario:
  Newly retired
  Desire to live in a log cabin (532 ft2)
  Rainwater Harvesting to be sole water source
http://www.rain-barrel-world.com/rainwater-cisterns.html

## Slide 4: Methodology
Utilize available Monthly data from PRISM
Determine catchment area and monthly water usage
Model end of Month Storage based on 30 yr average precipitation data
Model year-end Storage
Assume Limitless Tank

## Slide 5: Desired End-state
A spatial representation of water available anywhere in the US based on:
  Catchment area
  Monthly Usage
Ability to quickly view when periods of low storage may occur and plan accordingly

## Slide 6: Methodology
Data Source:
Monthly Avg. Data 1971-2000
GIS Model:
Projection: GCS_North_American_1983

## Slide 7: Methodology continued….
Storage Calculation:
Result is a Raster for End of Month Storage
Where:
S= Storage available(gal)
PV=Prism Precipitation value(100mm)
CA=Catchment Area (ft2 )
M= Monthly water Usage(gal)
=efficiency factor (.85)

## Slide 8: End of Month Storage Rasters (January)
Gallons of Water
532 ft2 Catchment
1000 gallons/mo. usage
2000 ft2 Catchment
1000 gallons/mo. usage

## Slide 9: End of Year Storage Raster
Gallons of Water
Ideal for Harvesting

## Slide 10: End of Year Storage Raster
Gallons of Water
Looks like a nice little hidden spot…..

## Slide 11: Capabilities
Rio Grande National Forest, Mineral County Colorado
Can zoom down to area you would like to live

## Slide 12: Limitations and Considerations
No Differentiation from snowfall to rainfall
Must still plan for droughts
Desired total storage
  Personal Use vs. Livestock
http://www.in.nrcs.usda.gov/smallscalefarmers
http://www.inarkansas.com/19996/woodlands-edge-shows-off-green-built-model-home

## Slide 13: References
Texas Water Development Board. 2005. “The Texas Manual on Rainwater Harvesting”
Texas Commission on Environmental Quality. January 2007. “Harvesting, Sorting, and Treating Rainwater for Domestic Indoor Use”

## Slide 14: Questions?
http://www.aquascapeinc.com/why_rainwater_harvesting