## Slide 1: Flood in Austin - Economic losses assesment
Alexandre Martinez
November, 16th 2011

## Slide 2: Introduction
Flood is the main cause of natural disaster losses in the USA.

## Slide 3: Introduction
What would be the economic impacts of flood in Austin ?
How different zones of Austin are threatned by flow?
Which part of Austin are threatened by flow?

## Slide 4: Economic assessment
Economic value Map
Land use of the city
Economic value of areas
Hazard Map
Floodplain
Vulnerability Relationships
Relationships between flood and losses

## Slide 5: Methodology

## Slide 6: Floodplain of City of Austin

## Slide 7: Floodplain of City of Austin
0.2 PCT Annual Chance Flood Hazard
A Zone
The base floodplain mapped by approximate methods, i.e., BFEs are not determined
AE Zone
X Zone
AO Zone
The base floodplain with sheet flow, ponding, or shallow flooding.
Zone X is the area determined to be outside the 500-year flood and protected by levee from 100-year flood.
Base flood depths (feet above ground) are provided
The base floodplain where base flood elevations are provided.
Areas subject to inundation by the 1-percent-annual-chance flood event.

## Slide 8: Land use of city of Austin : FIRMs

## Slide 9: Land use of city of Austin
Chart: Austin's Land use in 2008
| Undevelopped | Housing | Open space | Agriculture | Transport | Others | Water | Civic | Industrial | Commercial
 | 0.24365 | 0.24131 | 0.16326 | 0.10805 | 0.10389 | 0.038369 | 0.025549 | 0.025463 | 0.025427 | 0.02503

## Slide 10: Vulnerability
Losses
Tangible losses
Direct
Indirect
Intangible losses
Loss of production
Clean up
Structure
Inventories

## Slide 11: Vulnerability: Impact parameters
Flow velocity
For buildings
For agriculture
Flood depth
For buildings
For inventories
Flood duration
For inventories
For buildings

## Slide 12: Economic analysis : Computation of EAD.
Stage (H)
Discharge (Q)
Exceedance Probability (p)
Discharge (Q)
Stage (H)
Damage (D)
Exceedance Probability (p)
Damage (D)

## Slide 13: Economic analysis : Computation of EAD.
First Floor Elevation
h
Value of the building
Value of the content

## Slide 14: Economic analysis : Computation of EAD.

## Slide 15: Conclusion
Basic evaluation of the economic losses due to floods in urban areas:
  Land Use analysis
  Flood plain analysis
  Economic value of structure, inventories analysis
To Do:
  Inegrated theses 3 analysis in order to evaluate the losses for a 2% annual chance flood in the city of Austin.