## Slide 1: Hydrologic Information Systems to discover and combine data from multiple sources for hydrologic analysis
David Tarboton
Utah State University
Support
EAR 0622374
CUAHSI
HIS
Sharing hydrologic data
http://his.cuahsi.org/

## Slide 2: Outline
The CUAHSI HIS
  A Services-Oriented Architecture Based System for Sharing Hydrologic Data
  Including demo of HydroDesktop
HydroShare
  A Web-Based Collaborative Environment for the Sharing of Hydrologic Data and Models

## Slide 3
What proportion of your research time do you spend on preparing or preprocessing data into appropriate forms needed for research purposes?
http://his.cuahsi.org/documents/HISStatusSept15.pdf
Chart: 
| < 10 % | 10-25 % | 25-50 % | 50-75 % | > 75 % None
 | 18.6 | 45.7 | 24.3 | 11.4 | 0
Notes: Surveys of the hydrology community have indicated that data gathering and preprocessing is an inordinate fraction of the time required for modeling and analysis
In hydrology most of the easy single site, single variable, low hanging fruit research problems are solved and advances in understanding and better predictions require
combining information from multiple sources,
sharing and collaboration
Easier access to advanced computational capability
Sustainability and reliability in software

## Slide 4: Hydrologic Data Challenges
From dispersed federal agencies
From investigators collected for different purposes
Different formats
  Points
  Lines
  Polygons
  Fields
  Time Series
Rainfall and Meteorology
Water quantity
Soil water
Groundwater
Water quality
GIS
Data Heterogeneity
The way that data is organized can enhance or inhibit the analysis that can be done

## Slide 5: The way that data is organized can enhance or inhibit the analysis that can be done
I have your information right here …
Picture from: http://initsspace.com/

## Slide 6
Data Searching – What we used to have to do
NWIS
NARR
NAWQA
NAM-12
request
request
request
request
request
request
request
request
return
return
return
return
return
return
return
return
Searching each data source separately
Michael Piasecki
Drexel University
Notes: 6

## Slide 7
What HIS enables
Searching all data sources collectively
NWIS
NAWQA
NARR
generic
request
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
GetValues
ODM
Michael Piasecki
Drexel University
Notes: 7

## Slide 8
http://www.cuahsi.org
What is CUAHSI?
Support
EAR 0753521
109 US University members
7 affiliate members
20 International affiliate members
3 corporate members
(as of January 2013)
provides community and research support services to advance water research

## Slide 9: CUAHSI HIS
HydroServer – Data Publication
Lake Powell Inflow and Storage
HydroDesktop – Data Access and Analysis
HydroDesktop – Combining multiple data sources
HydroCatalog
Data Discovery
The CUAHSI Hydrologic Information System (HIS) is an internet based system to support the sharing of hydrologic data. It is comprised of hydrologic databases and servers connected through web services as well as software for data publication, discovery and access.

## Slide 10: HydroDesktop Demo
An open source
dotSpatial GIS based desktop client that supports discovery and analysis of hydrologic observations data

## Slide 11: HydroDesktop
Uses EPA WATERS Web, Mapping, and Database Services at http://www.epa.gov/waters/geoservices/index.html to delineate Watersheds
An open source
dotSpatial GIS based desktop client that supports discovery and analysis of hydrologic observations data
Notes: The service URLs that the HD tool uses are seen in http://hydrodesktop.codeplex.com/SourceControl/changeset/view/475b15a84bf4#Source%2fEPADelineation%2fCallWebService.cs The HD tool uses the Point Indexing Service to find the nearest NHD reach to where the user clicked. This returns a location on that reach. This point location is then used as input to the Navigation Delineation Service to get the watershed, and the Upstream/Downstream Service to get the river lines. The delineation service has two limitations: * It only works up to a certain distance upstream. I think we have it set to 100km. So for large watersheds (those with more than 100km of stream length upstream of where the user clicked), we don't get the most upstream portions of the watershed. * It doesn't delineate exactly to where the user clicked. It delineates to the endpoint of the NHD reach. (Can't remember if it is the clicked reach or the upstream reach -- try it and see.)

## Slide 12
Search last 22 years for all data in buffer around watershed

## Slide 13: Download and Plot the Data
Combining information from multiple sources

## Slide 14: Perform an analysis using R
At your fingertips
the full analysis capability of R
data from multiple sources
accessed from distributed (cloud) resources.
importance of interoperability

## Slide 15: Services-Oriented Architecture Paradigm of the World Wide Web
Catalog (Google)
Web Server
(CNN.com)
Browser
(Firefox)
Access
Crawl and Catalog
Search

## Slide 16: CUAHSI HIS Services-Oriented Architecture System for Sharing Hydrologic Data
Data Discovery and Integration
Data Publication
Data Analysis and Synthesis
HydroCatalog
HydroDesktop
HydroServer
Data Services
Metadata Services
Search Services
WaterML, Other OGC Standards
ODM
Geo Data
Information Model and Community Support Infrastructure

## Slide 17: Geographic Data Models
All geographic information systems are built using formal models that describe how things are located in space. A formal model is an abstract and well-defined system of concepts. A geographic data model defines the vocabulary for describing and reasoning about the things that are located on the earth. Geographic data models serve as the foundation on which all geographic information systems are built.
Scott Morehouse, Preface to “Modeling our World”, First Edition

## Slide 18: Geospatial Systems Are Helping Us Understand
. . . Helping Us Make Better Decisions
Data
Information
Knowledge
Understanding
Mapping
Integration
Sharing and Collaboration
From Jack Dangermond via David Maidment

## Slide 19: Hydrologic Science
Hydrologic conditions
(Fluxes, flows, concentrations)
Hydrologic Process Science
(Equations, simulation models, prediction)
Hydrologic Information Science
(Observations, data models, visualization
Hydrologic environment
(Physical earth)
Physical laws and principles
(Mass, momentum, energy, chemistry)
It is as important to represent hydrologic environments precisely with
data as it is to represent hydrologic processes with equations

## Slide 20: Data models capture the complexity of natural systems
NetCDF (Unidata) - A model for Continuous Space-Time data
Space, L
Time, T
Variables, V
D
Coordinate
dimensions
{X}
Variable dimensions
{Y}
ArcHydro – A model for Discrete Space-Time Data
Space, FeatureID
Time, TSDateTime
Variables, TSTypeID
TSValue
Terrain Flow Data Model used to enrich the information content of a digital elevation model
CUAHSI Observations Data Model: What are the basic attributes to be associated with each single data value and how can these best be organized?

## Slide 21: What are the basic attributes to be associated with each single data value and how can these best be organized?
Space, S
Time, T
Variables, V
s
t
Vi
vi (s,t)
“Where”
“What”
“When”
A data value
Variable
Method
Quality Control Level
Sample Medium
Value Type
Data Type
Source/Organization
Units
Accuracy
Censoring
Qualifying comments
Location
Feature of interest
Latitude
Longitude
Site identifiers
DateTime
Interval (support)

## Slide 22: Observations Data Model (ODM)
Soil
moisture
data
Streamflow
Flux tower data
Groundwater
levels
Water Quality
Precipitation
& Climate
A relational database at the single observation level
Metadata for unambiguous interpretation
Traceable heritage from raw measurements to usable information
Promote syntactic and semantic consistency
Cross dimension retrieval and analysis
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment, and I. Zaslavsky (2008), A relational model for environmental and water resources data, Water Resources Research, 44, W05406, doi:10.1029/2007WR006392.
Provides a common persistence model for data storage

## Slide 23
Horsburgh, J. S., D. G. Tarboton, D. R. Maidment and I. Zaslavsky, (2008), A Relational Model for Environmental and Water Resources Data, Water Resour. Res., 44: W05406, doi:10.1029/2007WR006392.
CUAHSI Observations Data Model http://his.cuahsi.org/odmdatabases.html
Notes: In designing ODM we asked: What are the basic attributes to be associated with each single data value and how can these best be organized? This involved community survey at a workshop and by email and based on the feedback received we came up with the ODM schema illustrated, published last year in WRR
This is quite a detailed slide, but it is the entire schema. Few database designs are simple enough to fit the entire schema on one slide. This shows at the center the data values table and off to the sides, the ancillary or metadata tables that record.

## Slide 24: Discharge, Stage, Concentration and Daily Average Example

## Slide 25: Site Attributes
SiteCode, e.g. NWIS:10109000
SiteName, e.g. Logan River Near Logan, UT
Latitude, Longitude Geographic coordinates of site
LatLongDatum Spatial reference system of latitude and longitude
Elevation_m Elevation of the site
VerticalDatum Datum of the site elevation
Local X, Local Y Local coordinates of site
LocalProjection Spatial reference system of local coordinates
PosAccuracy_m Positional Accuracy
State, e.g. Utah
County, e.g. Cache

## Slide 26
Feature
Waterbody
HydroID
HydroCode
FType
Name
AreaSqKm
JunctionID
HydroPoint
HydroID
HydroCode
FType
Name
JunctionID
Watershed
HydroID
HydroCode
DrainID
AreaSqKm
JunctionID
NextDownID
ComplexEdgeFeature
EdgeType
Flowline
Shoreline
HydroEdge
HydroID
HydroCode
ReachCode
Name
LengthKm
LengthDown
FlowDir
FType
EdgeType
Enabled
SimpleJunctionFeature
1
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
*
1
*
HydroNetwork
*
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
HydroJunction
HydroID
HydroCode
NextDownID
LengthDown
DrainArea
FType
Enabled
AncillaryRole
1
1
CouplingTable
SiteID
HydroID
Sites
SiteID
SiteCode
SiteName
Latitude
Longitude
…
Observations Data Model
1
1
OR
Independent of, but can be coupled to Geographic Representation
ODM
e.g. Arc Hydro

## Slide 27: Stage and Streamflow Example
Notes: Discharge Derived from Gage Height
Concepts:
Data derived from other data – single data point derived from a single observation (discharge from stage)
Data derived using a specific method (discharge from stage using rating curve)
Relationships:
Relationships between Values table and DerivedFrom table on DerivedFromID and ValueID
Relationship between Values table and Variables table on VariableID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID

## Slide 28: Water Chemistry from a profile in a lake
Notes: Water Chemistry From a Lake Profile
Concepts:
Grouped observations (all observations in one reservoir profile)
Observations made using an offset (observations made at multiple depths below the surface of a reservoir)
Observations made using a specific method (observations made using a particular field instrument)
Relationships:
Relationship between Values table and the Variables table on VariableID
Relationship between Values table and OffestTypes table on OffsetTypeID
Relationship between Values table and Methods table on MethodID
Relationship between Variables table and Units table on UnitID
Relationship between GroupDescriptions table and Groups table on GroupID
Relationship between OffsetTypes table and Units table on UnitID and OffsetUnitID

## Slide 29: Loading data into ODM
Interactive OD Data Loader (OD Loader)
  Loads data from spreadsheets and comma separated tables in simple format
Scheduled Data Loader (SDL)
  Loads data from datalogger files on a prescribed schedule.
  Interactive configuration
SQL Server Integration Services (SSIS)
  Microsoft application accompanying SQL Server useful for programming complex loading or data management functions
OD Data Loader
SDL
SSIS

## Slide 30: Importance of the Observations Data Model
Provides a common persistence model for observations data
Syntactic consistency (File types and formats)
Semantic consistency
  Language for observation attributes (structural)
  Language to encode observation attribute values (contextual)
Publishing and sharing research data
Metadata to facilitate unambiguous interpretation
Enhance analysis capability

## Slide 31
Set of query functions
Returns data in WaterML
WaterML and WaterOneFlow
WaterML is an XML language for communicating water data
WaterOneFlow is a set of web services based on WaterML
GetSites
WaterOneFlow
Web Service
GetValues
GetSiteInfo
GetVariableInfo
Notes: 31

## Slide 32
http://www.opengeospatial.org/standards/waterml
Open Geospatial Consortium Web Service Standards
This document is an OGC® Encoding Standard for the representation of hydrological observations data with a specific focus on time series structures.
These standards have been developed over the past 10 years …. by 400 companies and agencies ....

## Slide 33: HydroServer – Data Publication
Ongoing Data Collection
Data presentation, visualization, and analysis through Internet enabled applications
Internet Applications
Point Observations Data
Historical Data Files
GIS Data
ODM Database
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
OGC Spatial Data Service from ArcGIS Server
Notes: A platform for publishing space-time hydrologic datasets that:
  Autonomous with local control of data
  Part of a distributed system that makes data universally available
Basis for Experimental Watershed or Observatory data management system
Standards based approach to data publication
  Accepted and emerging standards for data storage and transfer (OGC, WaterML)
Built on established software
  MS SQL Server, ArcGIS server
Open Source Community Code Repository
  Sustainability

## Slide 34
HydroCatalog
GetSites
GetSiteInfo
GetVariableInfo
GetValues
WaterOneFlow
Web Service
WaterML
Discovery and Access
Hydro
Desktop
Water Metadata Catalog
Harvester
Service Registry
Hydrotagger
Search Services
http://hiscentral.cuahsi.org
Search over data services from multiple sources
Supports concept based data discovery
CUAHSI Data Server
3rd Party Server
e.g. USGS

## Slide 35: A growing collection of HydroServers and community of users
Dry Creek Experimental Watershed (DCEW) (28 km2 semi-arid steep topography, Boise Front)
68 Sites
24 Variables
4,700,000+ values
Published by Jim McNamara, Boise State University
University of Maryland, Baltimore County
Montana State University
University of Texas at Austin
University of Iowa
Utah State University
University of Florida
University of New Mexico
University of Idaho
Boise State University
University of Texas at Arlington
University of California, San Diego
Idaho State University

## Slide 36: A growing collection of HydroServers and community of users
Chart: 
| 2008 | 2009 | 2010 | 2011 | 2012 | 2013
New Networks | 27 | 9 | 13 | 21 | 27 | 18
Total Networks | 27 | 36 | 49 | 70 | 97 | 115
Server Networks Registered at HIS Central
Chart: 
| 2009 | 2010 | 2011 | 2012
Daily Average GetValue Requests | 361 | 964 | 11805 | 26772
Total GetValue Reqeusts | 132054 | 352149 | 4309039 | 9772023
Get Values Requests

## Slide 37: Open Development Model
http://hydrodesktop.codeplex.com
http://hydroserver.codeplex.com
http://hydrocatalog.codeplex.com

## Slide 38: CUAHSI HIS: A common window on water observations data for the United States unlike any that has existed before
Storage in a community data model
Publication from a server
Data access through internet-based services using consistent language and format
Tools for access and analysis
Discovery through thematic and geographic search functionality
Integrated modeling and analysis combining information from multiple sources
Server
Desktop
Catalog

## Slide 39: HydroShare - A web-based collaborative environment for the sharing of hydrologic data and models
beta.hydroshare.org
Can sharing data and models be as easy as sharing photos on Facebook or videos on YouTube?
Can finding data and models be as easy as shopping on Amazon?
Currently in beta testing. First release due next year
Notes: HydroShare will be a collaborative environment for sharing hydrologic data and models aimed at giving hydrologists the technology infrastructure they need to address critical issues related to water quantity, quality, accessibility, and management.
HydroShare will expand the data sharing capability of the CUAHSI Hydrologic Information System by broadening the classes of data accommodated, expanding capability to include the sharing of models and model components, and taking advantage of emerging social media functionality to enhance information about and collaboration around hydrologic data and models.
Functionality will include
A web portal for model and data sharing
Sharing features added to HydroDesktop client software
Access to more types of hydrologic data using standards compliant data formats and interfaces
Enhanced catalog functionality that broadens discovery functionality to different data types and models
New model sharing and discovery functionality
Enhanced easy to use access to high performance computing
Social media and collaboration functionality
Linkages to other data and modeling systems such as USGS and CUAHSI data services, NASA earth exchange and HPC resources e.g. at CSDMS

## Slide 40: HydroShare Functionality to be Developed
A new, web-based system for advancing model and data sharing
Sharing features to HydroDesktop
Access more types of hydrologic data using standards compliant data formats and interfaces
Enhance catalog functionality that broadens discovery functionality to different data types
New model sharing and discovery functionality
Facilitate and ease access to use of high performance computing
New social media and collaboration functionality
Links to other data and modeling systems

## Slide 44: Upload

## Slide 45: Imagine the Possibilities…
Observers and instruments
Data
Analysis
Models
Collaboration
HydroShare to support integrated collaborative analysis, modeling and data publication
HydroServer (ODM)
1
2
Observe
Publish and Catalog
3
Discover and Analyze/Model (in Desktop or Cloud)
Publication, Archival, Curation

## Slide 46
Observers and instruments
Data
Analysis
Models
Collaboration
HydroShare to support integrated collaborative analysis, modeling and data publication
Share the results (Data and Models)
HydroShare resource
store
4
Publication, Archival, Curation
Imagine the Possibilities…

## Slide 47: Imagine the Possibilities…
Observers and instruments
Data
Analysis
Models
Collaboration
HydroShare to support integrated collaborative analysis, modeling and data publication
Group Collaboration using HydroShare
Preparation of a paper
5
6
Publication, Archival, Curation

## Slide 48: Imagine the Possibilities…
Observers and instruments
Data
Analysis
Models
Collaboration
HydroShare to support integrated collaborative analysis, modeling and data publication
Submittal of paper, review, archival of electronic paper with data, methods and workflow
7
Publication, Archival, Curation
DataOne, EarthCube, …

## Slide 49: HydroShare Modeling
Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs (TauDEM + CyberGIS)
Preconfigured models and modeling systems as services (CI-WATER)
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for visualization and analysis
Automated reasoning to couple models based on purpose, context, data and resources (Aaron Byrd)
x
y
t
Flow
Time
Notes: Data: Links to national and global data sets of essential terrestrial variables (e.g. NASA NEX, HydroTerre)
Tools to preprocess and configure inputs
Preconfigured models and modeling systems as services
Standards for information exchange for interoperability (OpenMI, CSDMS BMI)
Tools for Visualization and Analysis
Automated reasoning to couple models based on purpose, context, data and resources

## Slide 50: Resource Repository Centric Paradigm for Modeling and Analysis
Enable multiple models to use common “best practice” tools
Analysis Tools
Visualization Tools
Data Loaders
Data Discovery Tools
Models
Resource Repository

## Slide 51: E.g. SWATShare
A web based tool for publishing, sharing, and accessing Soil Water Assessment Tool (SWAT)
www.water-hub.org/swat-tool
Notes: You need to log-in to use the functions of SWAT share. On this slide, you see a map the watershed in red are the one for which SWAT models are available. Once you click a on one of the watersheds (highlighted in yellow), then you see then you see the associated metadata with the model. If the model is only published (and not shared), one cannot download or run the model. However, if the model is published and shared, any user can download, modify, and run the model on the SWATShare.

## Slide 52: Model pre and post processing workflow
Each model interacts with information in the common data store
The modeler does not need to be concerned with and can take advantage of standardized analysis, visualization loading and discovery tools
Resource Repository
Analysis Tools
Visualization Tools
Data Loaders
Data Discovery Tools
Models
Resource Repository
Pre-Processing
Post -Processing
Input Files
Output Files
Model

## Slide 53: Architecture and Development

## Slide 54: Drupal – Content Management System
Extensible Open Source Content Management Framework for Publication written in PHP
  Over 14,000 user contributed modules
Themed and Styled Presentation of HydroShare Resources with in page visualization
Off the shelf modules provide a Social Experience surrounding Hydrologic Data: Comments, Ratings, Group Behavior
Custom module development supports HydroShare Data Model, GeoAnalytics and iRODS Integration

## Slide 55: Summary
To boldly go where no one has gone before
CUAHSI HIS
  Enhanced Access to Hydrologic Data
  Combining information from multiple sources
HydroShare
  A collaborative website for the sharing of hydrologic data and models
  To expand data sharing capability of CUAHSI HIS
    Additional data classes
    Models, scripts, tools and workflows
Ingredients for success
  Community participation
  Interoperability
  Standards
  Open Development

## Slide 56: Thanks to a lot of people
  USU
  RENCI/UNC
  CUAHSI
  BYU
  Tufts
  USC
  Texas
  Purdue
  SDSC
HydroShare team: Dave Tarboton, Ray Idaszak, Dan Ames, Jeff Horsburgh, Jon Goodall, Larry Band, Venkatesh Merwade, Jeff Heard, Carol Song, Alva Couch, David Valentine, Rick Hooper, Jennifer Arrigo, David Maidment, Tim Whiteaker, Alex Bedig, Laura Christopherson, Pabitra Dash, Tian Gan, Tony Castronova, Karl Gustafson, Stephen Jackson, Cuyler Frisby, Stephanie Mills, Brian Miles, Jon Pollak, Stephanie Reeder, Ash Semien, Yaping Xiao, Lan Zhao
http://www.cuahsi.org/hydroshare.aspx
OCI-1148453
OCI-1148090
Notes: The HydroShare project is part of a broad effort in CUAHSI in the area of Hydrologic Information Systems. We have a team of developers and domain scientists from eight universities working on HydroShare. This is part of the even broader focus in NSF on data management, Cyberinfrastructure and sustainable software.

## Slide 57: Are there any questions ?
AREA 1
AREA 2
3
12