## Slide 1: Hydro Networks in GIS
Review of key concepts in Ex 4
Connecting the Land and Water Systems
Hydrologic networks
Linear referencing on networks

## Slide 2: Reading (1)
What are geometric networks, A quick tour of geometric networks, Essential geometric networks
http://resources.arcgis.com/en/help/main/10.2/index.html#/What_are_geometric_networks/002r00000001000000/

## Slide 3: Reading (2)
- What is linear referencing; Essential linear referencing vocabulary
http://resources.arcgis.com/en/help/main/10.2/index.html#/What_is_linear_referencing/003900000001000000/

## Slide 4: Key Concepts from Exercise 4 Raster Analysis Layers
Fill
Flow Direction
Flow Accumulation
Stream Definition
Stream Links
Catchments

## Slide 5
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Grid
Streams
Vector
Streams

## Slide 6
Relationships linking Catchments and Drainage Lines

## Slide 7: Vector Analysis Layers
Vector streams
Vector catchments
Attribute feature with raster zonal statistics
Geometric Network
Tracing
Selection statistics

## Slide 8: Raster to Vector Transition
During the first part of Ex4, you are dealing with the flow of water through the landscape based on the raster data structures
During the last part of Ex 4 we are using vector network data to describe water pathways.
We will connect the land and water flow systems by attaching the catchments and watersheds derived from raster data processing to our vector networks

## Slide 9: Flow Line
Traces movement of water in a one-dimensional flow system

## Slide 10: Location of the Flowline

## Slide 11: Four Key Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 12: Cell Flows to a Cell
Core concept of flow on digital elevation models

## Slide 13: Line Flows to a Line
Geometric Network of NHDFlowlines

## Slide 14: Area Flows to a Line
Reach Catchments from NHDPlus
Flowline and Catchment have the same COMID

## Slide 15: Area Flows to a Point on a Line
Watersheds for USGS Gages
Tesselation using gage points

## Slide 16: Area Flows to a Point on a Line
Tesselation using Water Rights Diversion Points

## Slide 17: Topology
Topology (from the Greek τόπος, "place", and λόγος, "study") is the mathematical study of shapes and spaces. It is a major area of mathematics concerned with the most basic properties of space, such as connectedness, continuity and boundary. It is the study of properties that are preserved under continuous deformations including stretching and bending, but not tearing or gluing.
http://en.wikipedia.org/wiki/Topology
Connection by relationship Connection by geometry

## Slide 18: Connection by relationship
Area 354 flows to point 354

## Slide 19: Connection by Geometry
A network is a set of edges and junctions that are topologically connected to each other.

## Slide 20: Network Model in GIS
Three components
  Geometric model: (x,y,z,m) coordinates of edges and junctions
  Logical model: which edges are connected to what junctions
  Addressing model: location on the network using measure

## Slide 21: Edges and Junctions
Simple feature classes: points and lines
Network feature classes: junctions and edges
Edges can be
  Simple: one attribute record for a single edge
  Complex: one attribute record for several edges in a linear sequence
A single edge cannot be branched
No!!

## Slide 22: Polylines and Edges

## Slide 23: Junctions
Junctions exist at all points where edges join
  If necessary they are added during network building (generic junctions)
Junctions can be placed on the interior of an edge e.g. stream gage
Any number of point feature classes can be built into junctions on a single network

## Slide 24: Connectivity Table
J124
J125
J123
J126
E1
E3
E2
J123 | J124, E1 |  | 
J124 | J123, E1 | J125, E2 | J126, E3
J125 | J124, E2 |  | 
J126 | J124, E3 |  | 
Junction
Adjacent Junction and Edge
This is the “Logical Network”

## Slide 25: Build Network Tables
Establishes connectivity of Edge and Junction features
Enables tracing
Generates Generic Junctions
Geometric Network Wizard in ArcCatalog

## Slide 26: Snapping Features

## Slide 28: Network Sources and Sinks
Each junction
feature class
in a network can
have junctions
which are sources
or sinks for flow
Use complex edge so that junction can be interior to edge

## Slide 29: Flow to a sink

## Slide 30: Flags

## Slide 31: Trace Solvers

## Slide 32: Upstream Trace Solvers

## Slide 33: Water Rights in Luling, Tx
111 water right points upstream from Luling
54 water right points downstream from Luling
Trace Upstream
Trace Downstream

## Slide 34: Addressing

## Slide 35: Coordinates of a 2-D Polyline

## Slide 36: Coordinates of a 2-D Polyline M

## Slide 37: Setting Percent Measure
pMSeg.SetAndInterpolate
MsBetween 0, 100
pMSeg.SetAndInterpolate
MsBetween 100, 0
0 – 100 going upstream
0 – 100 going downstream

## Slide 38: Point and Line Events

## Slide 39: Longitudinal River Profile
Absolute Measure (Ma)
Relative Measure (Mr) = Ma/L

## Slide 40: Summary Concepts
Four key constructs
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 41: Summary Concepts (2)
A network is a connected set of points (junctions) and lines (edges) that supports tracing functions
  Three data model components
    Geographic (x,y,z)
    Logical (point-line topology connections)
    Addressing (position m along the line)