## Slide 1: Hydraulic Routing in Rivers
Reference: HEC-RAS Hydraulic Reference Manual, Version 4.1,
Reading: HEC-RAS Manual pp. 3-1 to 3-13
http://www.hec.usace.army.mil/software/hec-ras/documentation/HEC-RAS_4.1_Users_Manual.pdf

## Slide 2: Flood Inundation

## Slide 3: Floodplain Delineation
Notes: The channel and floodplain are both integral parts of the natural conveyance of a stream. The floodplain carries flow in excess of the channel capacity. The greater the discharge, the greater the extent of inundation. …. Because of its devastating nature, flooding poses serious hazards to human populations in many parts of the world. “The Flood Disaster Protection Act of 1973” required the identification of all floodplain areas in the United States and the establishments of flood-risk zones within those areas.

## Slide 4: Steady Flow Solution

## Slide 5
Right Overbank
Left Overbank
Channel centerline
and banklines
Cross-section
One-Dimensional Flow Computations

## Slide 6: Flow Conveyance, K
Left Overbank
Right Overbank
Channel

## Slide 7: Reach Lengths
(1)
(2)
Lob
Rob
Lch
Floodplain
Floodplain
Left to Right looking downstream

## Slide 8: Energy Head Loss

## Slide 9: Velocity Coefficient, 

## Slide 10: Solving Steady Flow Equations
All conditions at (1) are known, Q is known
Select h2
compute Y2, V2, K2, Sf, he
Using energy equation (A), compute h2
Compare new h2 with the value assumed in Step 2, and repeat until convergence occurs
h2
(2)
(1)
h1
Q is known throughout reach
(A)

## Slide 11: Flow Computations
Reach 2
Reach 3
Reach 1
Start at the downstream end (for subcritical flow)
Treat each reach separately
Compute h upstream, one cross-section at a time
Use computed h values to delineate the floodplain

## Slide 12: Floodplain Delineation
Notes: Ideally should have Two D Models…... A floodplain delineation process determines inundation extent by comparing water levels with ground surface elevations. We start with a DTM or topomap. > Water levels are computed based on cross-sections. During normal condition, flow remains within the main channel, but > during flood, water spill over the bank. In these cases it’s important to extent cross-section over the floodplain. > We then bring back water levels on the topomap. > Extent water levels until hit contour of higher elevations. > Finally delineate floodplain following the contours. The accuracy largely depends on water levels and in turns on the cross-section used for computation.

## Slide 13: Momentum Equation
Steady, uniform flow
Steady, non-uniform flow
Unsteady, non-uniform flow

## Slide 14: HMS-RAS Integration Strategy/Workflow Brushy Creek Example Dean Djokic, ESRI 22 March 2012

## Slide 15: Lecture Overview
Approach to integrated H&H model development
Upper Brushy Creek – GeoHMS/HMS development
Flood modeling for area of interest – GeoRAS/RAS development

## Slide 16: HMS-RAS Integration Overview

## Slide 17: Integration Approach
Mix of planning, GIS, and H&H modeling operations – not a push button operation.
Types of integration
  Modeling support (preparing data for model input)
    e.g. land use/soils/CN or rainfall processing – Arc Hydro or general GIS data processing
  Linked
    GeoHMS
    GeoRAS
  Integrated
    DSS

## Slide 18: Integration Approach (2)
Key steps:
  Plan (roughly) hydrologic and hydraulic model layouts – flow exchange locations
    e.g. location of HMS modeling elements and RAS cross-sections
  Identify sources of precipitation input into the hydrologic model and techniques for their incorporation into the dataset
    e.g. Nexrad rainfall
  Develop GeoHMS model (and precipitation sub model)
  Finalize and run HMS model and generate results (DSS)
  Develop GeoRAS model
  Finalize and run RAS taking HMS results as input
  Feedback between HMS and RAS is manual
    e.g. modification of time of concentration or routing parameters

## Slide 19: Integration Planning
Identify where outputs from one model (HMS) become input to the second one (RAS)
  Place hydrologic elements (subbasins, reaches, junctions) to capture flows at points of interest (confluences, structures)
  Place hydraulic elements (cross-sections) at points of interest
  Identify/specify element naming conventions between the two models (persistent or transient names)

## Slide 20: Precipitation Sources
Identify sources of precipitation input into the hydrologic model and techniques for their incorporation into the dataset
  Point (rain gage)
  Polygon (Nexrad cells)
  Surface (TIN/grid)

## Slide 21: Develop GeoHMS model
Follow all principles in development of a hydrologic model
In addition, take into consideration integration planning aspects developed earlier
  Placement of flow exchange points
  Naming conventions
Incorporate precipitation submodel
  Develop Arc Hydro time series for the final subbasin delineation and export to DSS
Export to HMS

## Slide 22: Meteorological Component
Develop a custom “gage” for each subbasin or for each rainfall observation element with corresponding weights for subbasins.
Export the time series for the subbasin “gage” from Arc Hydro time series data structure into DSS
Arc Hydro
DSS
Arc Hydro to DSS transfer

## Slide 23: Finalize and Run HMS
Complete HMS model with any additional parameters including meteorological model and control specifications
Follow all principles in HMS model development (calibration, etc.)

## Slide 24: Finalize and Run HMS (2)
Do the final run and generate results (DSS)
DSS View
HMS View

## Slide 25: Develop GeoRAS model (pre-processing)
Follow all principles in development of a hydraulic model for element placement (confluences, structures, …)
In addition, take into consideration integration planning aspects developed earlier
  Naming conventions (add name of the HMS element to the cross-section that will get the element’s flows)
Export to RAS

## Slide 26: Finalize and Run RAS
Complete RAS model with any additional parameters including initial and boundary conditions
Follow all principles in RAS model development (calibration, etc.)

## Slide 27: Finalize and Run RAS (2)
Do the final run and generate results (export to sdf file)

## Slide 28: Process RAS results in GeoRAS
Construct the floodplain based on the results in the sdf
Review the results with respect to spatial integrity (extents of cross-sections, ineffective flow areas, disconnected flood areas, …)
Clean results
Revisit RAS

## Slide 29: GIS – HMS – RAS Feedback
At present it is manual and at discretion of modeler
  GIS – H&H interaction
  H – H interaction
Visualization in both pre and post-processing – not just a “pretty picture”
  Fly-over in preprocessing (GeoHMS and GeoRAS)
    Identification of data problems
    Modeling element placement
  Post-processing (GeoRAS)
    Validity of element placement