## Slide 1: GIS in Water Resources Midterm Review 2013
David Maidment and David Tarboton

## Slide 2: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data

## Slide 3: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data

## Slide 4
Latitude and Longitude on a Spherical Earth
Longitude line (Meridian)
N
S
W
E
Range: 180ºW - 0º - 180ºE
Latitude line (Parallel)
N
S
W
E
Range: 90ºS - 0º - 90ºN
(0ºN, 0ºE)
Equator, Prime Meridian

## Slide 5: Origin of Geographic Coordinates
(0,0)
Equator
Prime Meridian

## Slide 6
Length on Meridians and Parallels (Spherical Earth)
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 7
Example: What is the length of a 1º increment along
on a meridian and on a parallel at 30N, 90W?
Radius of the earth = 6370 km.
Solution:
A 1º angle has first to be converted to radians
p radians = 180 º, so 1º = p/180 = 3.1416/180 = 0.0175 radians
For the meridian, DL = Re Df = 6370 * 0.0175 = 111 km
For the parallel, DL = Re Dl Cos f
= 6370 * 0.0175 * Cos 30
= 96.5 km
Parallels converge as poles are approached

## Slide 8: Shape of the Earth
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles

## Slide 9: Ellipse
P
F2
O
F1
a
b
X
Z


An ellipse is defined by:
Focal length = 
Distance (F1, P, F2) is
constant for all points
on ellipse
When  = 0, ellipse = circle
For the earth:
Major axis, a = 6378 km
Minor axis, b = 6357 km
Flattening ratio, f = (a-b)/a
~ 1/300

## Slide 10: Ellipsoid or Spheroid Rotate an ellipse around an axis
O
X
Z
Y
a
a
b
Rotational axis

## Slide 11: Horizontal Earth Datums
An earth datum is defined by an ellipse and an axis of rotation
NAD27 (North American Datum of 1927) uses the Clarke (1866) ellipsoid on a non geocentric axis of rotation
NAD83 (NAD,1983) uses the GRS80 ellipsoid on a geocentric axis of rotation
WGS84 (World Geodetic System of 1984) uses GRS80, almost the same as NAD83

## Slide 12: Definition of Latitude, f
(1) Take a point S on the surface of the ellipsoid and define there the tangent plane, mn
(2) Define the line pq through S and normal to the
tangent plane
(3) Angle pqr which this line makes with the equatorial
plane is the latitude f, of point S
O
f
S
m
n
q
p
r

## Slide 13: Cutting Plane of a Meridian
P
Meridian
Equator
plane
Prime Meridian

## Slide 14: Definition of Longitude, l
0°E, W
90°W
(-90 °)
180°E, W
90°E
(+90 °)
-120°
-30°
-60°
-150°
30°
-60°
120°
150°
l
l = the angle between a cutting plane on the prime meridian
and the cutting plane on the meridian through the point, P
P

## Slide 15
Global Positioning Systems
Distance to four satellites gives (x,y,z)
Notes: If we then make a measurement from a third satellite and find that we're 13,000 miles from that one, that narrows our position down even further, to the two points where the 13,000 mile sphere cuts through the circle that's the intersection of the first two spheres.
So by ranging from three satellites we can narrow our position to just two points in space.
To decide which one is our true location we could make a fourth measurement. But usually one of the two points is a ridiculous answer (either too far from Earth or moving at an impossible velocity) and can be rejected without a measurement.
A fourth measurement does come in very handy for another reason however, but we'll tell you about that later

## Slide 16: Revolution in Earth Measurement
Traditional Surveying uses benchmarks as reference points
Global Positioning uses fixed GPS receivers as reference points (Continuously Operating Reference System, CORS)
Some images and slides from Michael Dennis, National Geodetic Survey and Lewis Lapine, South Carolina Geodetic Survey

## Slide 17: HORIZONTAL TECTONIC MOTIONS
Pacific Plate
North American Plate
Motion in cm/year
When is California not in North America …
…. when its on the Pacific Plate!

## Slide 18: Representations of the Earth
Earth surface
Ellipsoid
~ Sea surface
Geoid
Geoid is a surface of constant
gravitational potential

## Slide 19: Definition of Elevation
Elevation Z
•
P
z = zp
z = 0
Mean Sea level = Geoid
Land Surface
Elevation is measured from the Geoid

## Slide 20: Vertical Earth Datums
A vertical datum defines elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
The National Elevation Dataset is in the NAVD88 datum
Heights are “elevation above datum”

## Slide 21: Geodesy and Map Projections
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data

## Slide 22: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 23: Types of Projections
Conic (Albers Equal Area, Lambert Conformal Conic) - good for East-West land areas
Cylindrical (Transverse Mercator) - good for North-South land areas
Azimuthal (Lambert Azimuthal Equal Area) - good for global views

## Slide 24
Projections Preserve Some Earth Properties
Area - correct earth surface area (Albers Equal Area) important for mass balances
Shape - local angles are shown correctly (Lambert Conformal Conic)
Direction - all directions are shown correctly relative to the center (Lambert Azimuthal Equal Area)
Distance - preserved along particular lines
Some projections preserve two properties

## Slide 25: Web Mercator Projection (used for ESRI Basemaps)
The spatial reference for the ArcGIS Online / Google Maps / Bing Maps tiling scheme is WGS 1984 Web Mercator (Auxiliary Sphere).
Web Mercator is one of the most popular coordinate systems used in web applications because it fits the entire globe into a square area that can be covered by 256 by 256 pixel tiles.

## Slide 26: Coordinate Systems
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin

## Slide 27: State Plane Coordinate System
Defined for each State in the United States
East-West States (e.g. Texas) use Lambert Conformal Conic, North-South States (e.g. California) use Transverse Mercator
Texas has five zones (North, North Central, Central, South Central, South) to give accurate representation
Greatest accuracy for local measurements

## Slide 28: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data

## Slide 29: What is GIS
A geographic information system (GIS) is a system designed to capture, store, manipulate, analyze, manage, and present all types of geographical data. -- Wikipedia
maps
data
tools
computers

## Slide 30: Geography is visualized in maps
www.arcgis.com
map

## Slide 31: Maps are built from data
map
data
Road
Name: E. Dean Keeton St
Type: Div Highway
Speed: 35 mph
Shape: [Geometry]
Building
Name: Ernest Cockrell Jr Hall
Address: 301 E. Dean Keeton St
Shape: [Geometry]
Shape includes the geometry of the feature and where it is located on earth

## Slide 32: Vector data represent discrete features
map
data
polygons
lines
points

## Slide 33: Raster data form a grid of cells or pixels
map
data

## Slide 34
Data Model
Conceptual Model – a set of concepts that describe a subject and allow reasoning about it
Mathematical Model – a conceptual model expressed in symbols and equations
Data Model – a conceptual model expressed in a data structure (e.g. ascii files, Excel tables, …..)
Geographic Data Model – a conceptual model for describing and reasoning about the world expressed in a GIS database

## Slide 35: Linking Geography and Attributes
GIS has a one to one association between a geographic feature and a record in an attribute table.
Geographic coordinates
Tabular attributes

## Slide 36
Data Model based on Inventory of data layers

## Slide 37
Image: Michael Zeiler, ESRI
Common Geospatial Information Types

## Slide 38
Raster and Vector Data
Point
Line
Polygon
Vector
Raster
Raster data are described by a cell grid, one value per cell
Zone of cells

## Slide 39: Geodatabase – a store for all types of geospatial information

## Slide 40
Geodesy, Map Projections and Coordinate Systems
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data
Spatial Reference = Datum + Projection + Coordinate system

## Slide 41: ArcGIS Spatial Reference Frames
Defined for a feature dataset in ArcCatalog
XY Coordinate System
  Projected
  Geographic
Z Coordinate system

## Slide 42: Horizontal Coordinate Systems
Geographic coordinates (decimal degrees)
Projected coordinates (length units, ft or meters)

## Slide 43: Key ArcGIS Software Components
ArcMap
ArcCatalog
ArcToolbox
Extensions
Geoprocessing

## Slide 44: Arc Toolbox
Map Projections
Tools for commonly used tasks

## Slide 45: Spatial Analyst
Analysis of land surface terrain as a grid
Key means of defining drainage areas and connectivity to stream network

## Slide 46: Geo-Processing
Toolbox tools linked together using the model builder to automate data processing

## Slide 47: Web-centered GIS
ArcGIS
Online

## Slide 48: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data
Remote Sensing

## Slide 49
x
y
f(x,y)
Two fundamental ways of representing geography are discrete objects and fields.
The discrete object view represents the real world as objects with well defined boundaries in empty space.
The field view represents the real world as a finite number of variables, each one defined at each possible position.
(x1,y1)
Points
Lines
Polygons
Continuous surface
Spatial Analysis Using Grids

## Slide 50
Numerical representation of a spatial surface (field)
Grid
TIN
Contour and flowline

## Slide 51
Grid Datasets
Cellular-based data structure composed of square cells of equal size arranged in rows and columns.
The grid cell size and extent (number of rows and columns), as well as the value at each cell have to be stored as part of the grid definition.
Number of columns
Number of rows
Cell size

## Slide 52
Raster Calculator
Cell by cell evaluation of mathematical functions

## Slide 53
Nearest Neighbor Resampling with Cellsize Maximum of Inputs
40
50
55
43
47
41
44
42
42
100 m
4
2
4
6
150 m
40-0.5*4 = 38
55-0.5*6 = 52
38
52
41
39
42-0.5*2 = 41
41-0.5*4 = 39

## Slide 54: Interpolation
Estimate values between known values.
A set of spatial analyst functions that predict values for a surface from a limited number of sample points creating a continuous raster.
Apparent improvement in resolution may not be justified

## Slide 55: Interpolation methods
Nearest neighbor
Inverse distance weight
Bilinear interpolation
Kriging (best linear unbiased estimator)
Spline

## Slide 56: Nearest Neighbor “Thiessen” Polygon Interpolation
Spline Interpolation

## Slide 57
Topographic Slope
Defined or represented by one of the following
  Surface derivative z
  Vector with x and y components
  Vector with magnitude (slope) and direction (aspect)

## Slide 58: ArcGIS “Slope” tool
a
b
c
d
e
f
g
h
i

## Slide 59
DEM Based Watershed and Stream Network Delineation Steps
DEM Reconditioning/Burning in Streams
Fill Sinks
Eight direction pour point model to evaluate flow directions
Flow accumulation
Threshold stream network definition
Stream segmentation
Watershed delineation
Raster to vector conversion of streams and watersheds

## Slide 60
Digital Elevation Model (DEM)-30 meter
National Elevation Dataset

## Slide 61
Filling in the Pits
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are filled they become sinks and isolate portions of the watershed
Pit filling is first thing done with a DEM

## Slide 62: Identifying and Removing Pits/Sinks in a DEM
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 5 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 5 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 8 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 7 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 7 | 6 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 7 | 7 | 8 | 9 | 15 | 15 | 8 | 15 | 15
15 | 8 | 8 | 8 | 7 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
5 | 5 | 4 | 5 | 5 | 5 | 5 | 3 | 5 | 5
6 | 6 | 5 | 6 | 6.1 | 5 | 6 | 6 | 6 | 6
7 | 7 | 6 | 7 | 7 | 4 | 7 | 6 | 7 | 7
9 | 9 | 8 | 9 | 9 | 3.9 | 9 | 6 | 9 | 9
11 | 11 | 10 | 11 | 11 | 11 | 11 | 9 | 11 | 11
12 | 12 | 9 | 12 | 12 | 12 | 12 | 10 | 12 | 12
13 | 12 | 9 | 12 | 13 | 13 | 13 | 11 | 13 | 13
14 | 9 | 9 | 11 | 14 | 14 | 14 | 12 | 14 | 14
15 | 9 | 9 | 9 | 9 | 15 | 15 | 12 | 15 | 15
15 | 9 | 9 | 9 | 9 | 16 | 16 | 14 | 16 | 16
15 | 11 | 9 | 11 | 11 | 17 | 17 | 17 | 17 | 17
15 | 15 | 8 | 15 | 15 | 18 | 18 | 15 | 18 | 18
Contains pits
Filled
A pit is a set of one or more cells which has no downstream cells around it.

## Slide 63
67
56
49
52
48
37
58
55
22
30
67
56
49
52
48
37
58
55
22
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent

## Slide 64
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water flows in the direction of steepest descent

## Slide 65
Flow Accumulation Grid.
Area draining in to a grid cell
ArcHydro Page 72
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Flow Accumulation > Threshold

## Slide 66
Watershed Draining to Outlet

## Slide 67
Stream links grid for the San Marcos subbasin
172
201
204
202
206
203
209
Each link has a unique identifying number

## Slide 68: Review for Midterm Exam
Location on the Earth
ArcGIS as a Geographic Information System
Working with Raster Data
Working with Vector Data

## Slide 69
National Hydro Data Programs
National Elevation Dataset
(NED)
National Hydrography Dataset
(NHD)
Watershed Boundary Dataset
NED-Hydrology
Data Sources for GIS in Water Resources
What is it?
What does it contain?
What is the GIS format?
Where would it be obtained

## Slide 70: Watershed Boundary Dataset for Nebraska
2990 HUC12 watersheds of average area 39.3 square miles
HUC12:HUC8 ~ 40:1 watersheds
Notes: HUCs are important for estimating water supply, water quality, and runoff. They are building blocks of water studies

## Slide 71
http://www.soils.usda.gov/survey/geography/ssurgo/
1:24,000 scale
soil information
SSURGO:
County Level
Digital Soil Maps

## Slide 72: Ssurgo for Lancaster County, NE
96 soil map units described by 18,565 polygons

## Slide 73
Same Cell Value
Catchments for Stream Links

## Slide 74
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams

## Slide 75
Raster Zones and Vector Polygons
Catchment Grid_code
Vector Polygons
Raster pixel value
Raster Zones
3
4
5
One to one connection

## Slide 76: Relationship
A relationship is an association or link between two objects in a database.
A relationship can exist between spatial objects (features in feature classes), non-spatial objects (objects in object classes), or between spatial and non-spatial objects.

## Slide 77
Relationships linking Catchments and Drainage Lines

## Slide 78: Zonal Average of Raster over Subwatershed joined to Subwatershed table
Join

## Slide 79
Catchment, Watershed, Subwatershed.
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 80: Connecting Land and Water
Four key ideas:
  Cell to cell water movement on DEMs
  Line to Line water movement on networks
  Area flows to line (connect land and water systems – Reach Catchments)
  Area flows to point on line (Watershed delineation from designated points)

## Slide 81: Cell Flows to a Cell
Core concept of flow on digital elevation models

## Slide 82: Line Flows to a Line
Geometric Network of NHDFlowlines

## Slide 83: Area Flows to a Line
Reach Catchments from NHDPlus
Flowline and Catchment have the same COMID

## Slide 84: Area Flows to a Point on a Line
Watersheds for USGS Gages

## Slide 85: Network Model in GIS
Three components
  Geometric model: (x,y,z,m) coordinates of edges and junctions
  Logical model: which edges are connected to what junctions
  Addressing model: location on the network using measure

## Slide 86: Connectivity Table
J124
J125
J123
J126
E1
E3
E2
J123 | J124, E1 |  | 
J124 | J123, E1 | J125, E2 | J126, E3
J125 | J124, E2 |  | 
J126 | J124, E3 |  | 
Junction
Adjacent Junction and Edge
This is the “Logical Network”

## Slide 87: Upstream Trace Solvers

## Slide 88
Network Tracing on the Guadalupe Basin

## Slide 89: Addressing