## Slide 1: Digital Elevation Model Based Watershed and Stream Network Delineation
How to use
Reading
https://pro.arcgis.com/en/pro-app/tool-reference/spatial-analyst/an-overview-of-the-hydrology-tools.htm
Understanding

## Slide 2: Topography defines watersheds which are fundamentally the most basic hydrologic landscape elements.

## Slide 3: Learning Objectives
To be able to delineate watersheds as the basic hydrologic model elements from Digital Elevation Models using Geographic Information Systems tools and to use this information in Hydrologic Analyses
Explain the basic concepts involved in the terrain flow information model
Identify and fill sinks in a small digital elevation model
Calculate hydrologic slope in the direction of steepest descent and the eight direction pour point model flow direction
Calculate flow accumulation as the number of grid cells draining into a grid cell
Identify a stream network raster based on grid cells exceeding a flow accumulation threshold
Describe the sequence of steps involved in mapping stream networks, catchments and watersheds in preparation for learning how to actually do this in the next exercise

## Slide 4: Outline
DEM Pit removal
Flow direction field derivation
Flow Accumulation
Channels and Watersheds
Raster to Vector Connection
Using vector stream information
DEM Conditioning
Hydrologic Terrain Analysis Software

## Slide 5: The starting point: a grid digital elevation model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 6: The terrain flow information model for deriving channels, watersheds, and flow related terrain information.
Raw DEM
Pit Removal (Filling)
Flow Field
Channels, Watersheds, Flow Related Terrain Information
Watersheds are the most basic hydrologic landscape elements
Notes: This slide shows the general model for deriving flow field related derivative surfaces from digital elevation data. The input is a raw digital elevation model, generally elevation values on a grid. This is basic information used to derive further hydrology related spatial fields that enrich the information content of this basic data. The first step is to remove sinks, either by filling, or carving. Then a flow field is defined. This enables the calculation of flow related terrain information. My focus has been on flow related information working within this framework. I try to leave other GIS functionality, like radiation exposure, line of sight analyses and visualization to others. I have distributed my software in ways that it easily plugs in to mainstream systems, such as ArcGIS to enhance ease of use.

## Slide 7: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 8: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 9: Pit Filling
Original DEM
Pits Filled
Pits
Grid cells or zones completely surrounded by higher terrain
Pour Points
The lowest grid cell adjacent to a pit

## Slide 11
80
74
63
69
67
56
60
52
48
30
D8 Flow Direction Model
- Direction of steepest descent
Slope = Drop/Distance
Steepest down slope direction
32
16
8
64
4
128
1
2

## Slide 12
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Eight Direction (D8) Flow Model
32
16
8
64
4
128
1
2

## Slide 13: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 14
Grid Network

## Slide 15
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell

## Slide 16
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation > 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area
Stream Definition

## Slide 17
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
2
5
15
20
2
The area draining each grid cell includes the grid cell itself.
1
1
1
1
1
1
1
2
1
1
1
1
1
1
3
3
3
11
2
1
5
2
2
20
15
TauDEM contributing area convention.

## Slide 18
4
5
6
3
7
2
1
8
ArcGIS and TauDEM flow direction encodings
TauDEM
32
16
8
64
4
128
1
2
ArcGIS

## Slide 19
Watershed Draining to Outlet
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 20: Watershed and Stream Grids
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 21
ArcHydro Page 74
172
201
204
202
206
203
209
Each link has a unique identifying number
Stream Segments
Maidment, D. R., ed. (2002), Arc Hydro GIS for Water Resources, ESRI Press, Redlands, CA, 203 p.

## Slide 22
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 23
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 24: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 25: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 26
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 27
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 28: Using Vector Stream Information
+
=
 Take a mapped stream network and a DEM
 Make a grid of the streams
 Raise the off-stream DEM cells by an arbitrary elevation
increment
 Produces "burned in" DEM streams = mapped streams
“Burning In” the Streams

## Slide 29
AGREE Elevation Grid Modification Methodology – DEM Reconditioning

## Slide 30: Carving
Lower elevation of neighbor along a predefined drainage path until the pit drains to the outlet point

## Slide 31: Carving
Pits
Carve outlets
Original DEM
Carved DEM
Notes: Elevations are filled to that of the pools pour point

## Slide 32
Filling
Carving
Minimizing Alterations

## Slide 33: Minimizing DEM Alterations
Optimally adjusted
Pits
Original DEM
Carved
Filled
Notes: Elevations are filled to that of the pools pour point

## Slide 34: Summary of Key Processing Steps
[DEM Reconditioning]
Pit Removal (Fill Sinks)
Flow Direction
Flow Accumulation
Stream Definition
Stream Segmentation
Catchment Grid Delineation
Raster to Vector Conversion (Catchment Polygon, Drainage Line, Catchment Outlet Points)

## Slide 35: Hydrologic Terrain Analysis Software
ArcGIS Portal ready to use tools
ArcGIS Hydrology Tools
ArcHydro
TauDEM
[RiverTools]
[GRASS]

## Slide 36: ArcGIS Pro Ready to Use Tools

## Slide 37: ArcGIS Hydrology Toolset

## Slide 38: ArcHydro
http://resources.arcgis.com/en/communities/hydro/

## Slide 39: TauDEM
Stream and watershed delineation
Multiple flow direction flow field
Calculation of flow based derivative surfaces
MPI Parallel Implementation for speed up and large problems
Open source platform independent C++ command line executables for each function
Deployed as an ArcGIS Toolbox with python scripts that drive command line executables
CSDMS Cluster Implementation
Open Topography implementation
CyberGIS Implementation
http://hydrology.usu.edu/taudem/

## Slide 40: Workflow to automatically generate stream network upstream of outlet

## Slide 41: Catchments linked to Stream Network
The starting point for catchment based distributed hydrologic modeling

## Slide 42: Edge contamination
Edge contamination arises when a contributing area value depends on grid cells outside of the domain. This occurs when drainage is inwards from the boundaries or areas with no data values. The algorithm recognizes this and reports "no data" resulting in streaks of "no data" values extending inwards from boundaries along flow paths that enter the domain at a boundary.

## Slide 43: Summary Concepts
The eight direction pour point model approximates the surface flow using eight discrete grid directions
The elevation surface represented by a grid digital elevation model is used to derive surfaces representing other hydrologic variables of interest such as
  Slope
  Flow direction
  Drainage area
  Catchments, watersheds and channel networks
Software as a service approach is moving functionality into the cloud