## Slide 1: Hurricane Harvey: Flood Emergency Response
Hurricane Harvey
Flood forecasting
Texas Flood Response System
How can we do better?

## Slide 2: Real-Time Flood Inundation Mapping Onion Creek at Highway 183
http://water.weather.gov/ahps2/inundation/inundation_google.php?gage=atit2

## Slide 3: Rating Curve at a Stream Gage
Water Level
Discharge

## Slide 4: Texas Address Points
9.28 million points
Point on every building
used for dispatching
emergency response
vehicles by 911 systems
Notes: Over the summer we collected all 8.7million address points across Texas. Dr. David Arctur has assembled all the data and done some quality checks. When you have this much data from hundreds of sources, there are always some inconsistencies. However, in my opinion, for public safety this strategic snapshot is a good starting point for describing overall impact to a region or district.

## Slide 5: Method for Determining Flood Risk: Height Above Nearest Drainage (HAND)
HAND
Flood
Normal
Flooding occurs when Water Depth is greater than HAND
Address Point
Computed for continental US
Notes: How do we answer the question of how many people are going to be impacted, especially if large areas of the state are not covered by LIDAR or National Flood Hazard Layer? The researchers developed a process called Height Above Nearest Drainage or HAND.

## Slide 6: Reach Hydraulic Parameters
Comid | y | A | R | P | T | V | Ab | As
5781175 | 3 |  |  |  |  |  |  | 
5781175 | 4 |  |  |  |  |  |  | 
Wetted Bed Area
L
As
Ab
V
T
P
A
y
Surface Area
Volume
Depth
T
P
Cross Section Area
Wetted Perimeter
Top Width
R
Hydraulic Radius

## Slide 7: Flood Inundation Mapping – NHDPlus-HAND Method
Catchments and Flowlines
Digital Elevation Model
Height Above Nearest
Drainage (HAND) (relative elevation of land
surface cell above cell in
NHDPlus stream to which it flows)
Inundation map Height above
drainage < 15 ft)
NHDPlus
z
y
Water surface elevation
h = z + y
h
Geodetic datum

## Slide 8: Reach Catchment 5781289
Eanes Creek, Rollingwood, Texas
Drainage area = 3.13 mi2
Reach Length = 4.3 miles

## Slide 9: Rating Curve Computation
Hydraulic Radius, R
n = 0.035 Manning roughness of channel
So = 0.0163 Bed slope
Cross section Area, A
Flood Depth, h (ft)
Flood Discharge, Q (cfs)

## Slide 10: Rating Curve – Connects Discharge with Depth
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Chart: Rating Curve for Eanes Creek, ComID = 5781289
| 0 | 607.56406134719555 | 2490.8796015163871 | 5785.1592347077603 | 10565.65567829302 | 16808.943658196451 | 24277.138771673799
Stage Height, h (ft) | 0 | 2.0669 | 3.937 | 5.807 | 7.6443 | 9.4159 | 10.9907
Forecast Discharge, Q,
from National Water Model
Flood Depth, y (ft)

## Slide 11: Texas Flood Response System
Discharge
Depth
Inundation
Impact
Transform discharge to depth by rating curve
or hydraulic model
Create flood inundation map from water depth
Assess impact on people and property
Take discharge forecast from the National Water Model
Flood emergency response depends on assessment of impact

## Slide 12: Flood Impact from National Water Model forecast at 3PM Friday 25 August
Houston is going to get inundated
10 PM, Friday 25 August
Using National Water
Model Medium Range forecast

## Slide 13: Buildings Damaged Data: Texas Division of Emergency Management
Total = 152,800
NWM Predicted Top 5 Counties Harris
Fort Bend
Brazoria
Galveston Montgomery
Actual Top 5 counties
Harris Orange Fort Bend Montgomery Jefferson

## Slide 14: Texas Flood Response System correctly located the major damage zone before the hurricane reached the coast
Actual Damage
Forecast Damage

## Slide 15: 27,000 Texas bridges on 15,700 stream reaches forecast by the National Water Model
Flood forecasting system
for Texas Bridges

## Slide 16: Radar Measurement Technologies
Densified forecasting requires densified measurement
Measures water level
Measures surface velocity

## Slide 17: Radar Measurement of Discharge using RQ-30
Combine with Acoustic Doppler Current Profiler
velocity profile
to get discharge
Measure velocity at one
point on water surface

## Slide 18
Densified Measurements
ADCP
Humminbird Helix Radar
Sommer Radar
Images: John Sloat, WaterCube

## Slide 19: River Bathymetry and Velocity Maps

## Slide 20: Radar Streamflow Measurement on I-10
20 Sensors from San Antonio
to LA border

## Slide 21: “Internet of Water” using the WaterML language
XML
Colorado River at Austin
24/7/365 service
For daily and real-time data
http://waterservices.usgs.gov/nwis/iv/?format=waterml,2.0&sites=08158000&period=P1D&parameterCd=00060
WaterML2 is the international standard internet language for water resources times series…

## Slide 22: Internet of Water for New Zealand
Data from 16 regions and one national agency. . .
. . . all accessible through water data services
National synthesis without centralizing data
New Zealand
Water Information System

## Slide 23: City of Austin Flood Alert System
City of Austin gages
LCRA gages
USGS gages
Rainfall and Water Level gages
All gages accessed
by water data services

## Slide 24: Three-Tier Flood Alert System
Tier 1: Standard USGS Gages
– measure everything
Tier 2: Radar Sensors on Bridges (TxDOT)
– medium and high flows
Tier 3: Water Level Sensors
– local flood alert systems
Cost
All connected using WaterML data services