## Slide 1: Watershed and Stream Network Delineation using GIS
CE 365K Spring 2016
http://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/an-overview-of-the-hydrology-tools.htm

## Slide 2: Components of a Drainage Basin

## Slide 3: National Elevation Dataset
Digital Elevation Model with 1 arc-second (30m), 1/3 arc-second (10m) and some 1/9 arc second (3m) cells
Distributed as part of the National Map
10 billion data
Derived from USGS 1:24,000 quadrangle sheets and at higher resolution from LIDAR
Get the data:
http://ned.usgs.gov/
http://nationalmap.gov/viewer.html

## Slide 4: National Elevation Dataset Availability
From http://nationalmap.gov/viewer.html

## Slide 5: Digital Elevation Model (DEM)
Contours
720
700
680
740
680
700
720
740
720
720

## Slide 6: Austin West 30 Meter DEM

## Slide 7
Digital Elevation Model (DEM)-30 meter

## Slide 8: Raster Digital Elevation Model (DEM)

## Slide 9: The challenge of increasing Digital Elevation Model (DEM) resolution
1980’s DMA 90 m
102 cells/km2
1990’s USGS DEM 30 m
103 cells/km2
2000’s NED 10-30 m
104 cells/km2
2010’s LIDAR ~1 m
106 cells/km2

## Slide 10: Hydrologic Modeling Flowchart

## Slide 11
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 12: The Pit Removal Problem
DEM creation results in artificial pits in the landscape
A pit is a set of one or more cells which has no downstream cells around it
Unless these pits are removed they become sinks and isolate portions of the watershed
Pit removal is first thing done with a DEM

## Slide 13: Pit Filling
Increase elevation to the pour point elevation until the pit drains to a neighbor

## Slide 14: Fill function
http://desktop.arcgis.com/en/arcmap/10.3/tools/spatial-analyst-toolbox/how-fill-works.htm

## Slide 15: Pit Filling
Pits
Pour Points
Original DEM
Pits Filled
Grid cells or zones completely surrounded by higher terrain
The lowest grid cell adjacent to a pit
Notes: Elevations are filled to that of the pools pour point

## Slide 17
32
16
8
64
4
128
1
2
Eight Direction Pour Point Model
Water in a given cell flows one or more of eight adjacent cells in the direction of steepest descent (ArcGIS)
ArcGIS raster operations involved in watershed delineation are derived from the premise that “water flows downhill, in doing so, will follow the steepest descent

## Slide 18
80
74
63
69
67
56
60
52
48
80
74
63
69
67
56
60
52
48
30
Slope:
Hydrologic Slope
- Direction of Steepest Descent
30

## Slide 19
2
2
4
4
8
1
4
16
1
2
4
8
4
4
1
2
4
8
2
4
4
4
4
2
1
Eight Direction (D8) Flow Model
32
16
8
64
4
128
1
2

## Slide 20: Flow Direction

## Slide 21: Flow Direction Grid
32
16
8
64
4
128
1
2

## Slide 22
Grid Network

## Slide 23
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
14
4
1
19
1
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation Grid.
Area draining in to a grid cell
Link to Grid calculator
ArcHydro Page 72

## Slide 24: Flow Accumulation

## Slide 25
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
10
1
0
1
4
14
19
1
Flow Accumulation > 10 Cell Threshold
0
0
0
0
0
0
0
1
0
0
0
0
0
0
2
2
2
1
0
4
1
1
10
14
19
Stream Network for 10 cell Threshold Drainage Area

## Slide 26
Watershed Draining to Outlet
Watershed mapped as all grid cells that drain to an outlet
Streams mapped as grid cells with flow accumulation greater than a threshold

## Slide 27
Vectorized Streams Linked Using Grid Code to Cell Equivalents
Vector
Streams
Grid
Streams
ArcHydro Page 75

## Slide 28
DrainageLines are drawn through the centers of cells on the stream links. DrainagePoints are located at the centers of the outlet cells of the catchments
ArcHydro Page 75

## Slide 29: Catchments
For every stream segment, there is a corresponding catchment
Catchments are a tessellation of the landscape through a set of physical rules

## Slide 30: Raster Zones and Vector Polygons
Catchment GridID
Vector Polygons
DEM GridCode
Raster Zones
3
4
5
One to one connection

## Slide 31
Catchments, DrainageLines and DrainagePoints of the San Marcos basin
ArcHydro Page 75

## Slide 32
Catchment, Watershed, Subwatershed.
ArcHydro Page 76
Watershed outlet points may lie within the interior of a catchment, e.g. at a USGS stream-gaging site.
Catchments
Subwatersheds
Watershed

## Slide 33: Delineation of Streams and Watersheds on a DEM

## Slide 34
http://srtm.usgs.gov/

## Slide 35: HydroSheds derived from SRTM
http://hydrosheds.cr.usgs.gov/

## Slide 37
LIDAR-Based Inundation Mapping

## Slide 38: USACE National Coastal Mapping Program
Jennifer M. Wozencraft, JALBTCX
Director, Joint Airborne Lidar Bathymetry Technical Center of Expertise
Program Manager, USACE National Coastal Mapping Program
15 October 2015
National Academies of Sciences, Engineering, and Medicine
Mapping Science Committee
Lidar workshop

## Slide 39
Seabrook, NH, federal navigation project and backbay marsh

## Slide 40
10,000 Hz Pulse Rate (hydro / topo)
0.4 Hz / 25 MP Digital camera (~20 cm pixel)
CASI-1500 Hyperspectral Imager
  1500 pixels
  380 – 1050 nm wavelength
  288 possible bands
15 cm RMSE bathymetry
7.5 cm RMSE topography
Shot spacing:
0.7 X 0.7 meter topo / shallow hydro
2.0 X 2.0 meter deep hydro
300 - 400 m op altitude (hydro)
300 - 1200 m op altitude (topo)
Shorter laser pulse length and receiver response for increased accuracy, especially in shallow (<2m) water
Large field-of-view afforded by prism, and more sensitive receivers, increase signal-to-noise ratio.
Improved depth detection in shallow turbid water
Dia: 290m
400 m
40

## Slide 41: Bathymetric lidar principle
RECEIVER FIELD OF VIEW
SEA SURFACE
SCATTERING AND
ABSORPTION
ILLUMINATED BOTTOM REGION
UNSCATTERED REF PATH
VERTICAL DEPTH
VOLUME BACKSCATTER
DIFFUSE
BOTTOM
REFLECTION
MEAN WATER
NADIR ANGLE
REFLECTED
BOTTOM
SIGNAL
INCIDENT LASER PULSE
SPECULAR
INTERFACE
REFLECTION
SURFACE REGION
IN RECEIVER FOV
ILLUMINATED
SURFACE
AREA
TIME
AMPLITUDE
Volume Backscatter
Detection
Points
t
Surface
(Interface)
Return
Bottom
Return

## Slide 42: FAQ’s
National Academies of Sciences of Sciences Engineering Medicine
Mapping Science Committee
LiDAR Workshop
Existing and future potential of high-accuracy LiDAR from high-altitude manned and unmanned platforms
Mark E. Romano
Sr. Product Manager
Space and Intelligence Systems

## Slide 43: What makes Geiger Mode so Different?
  Geiger-mode sensors sample the same spot on the ground thousands of times
Geiger Mode
Linear Mode

## Slide 44: Linear Mode LiDAR
Approximately 500 KHz sample rate for single scanner designs
Technology Comparison
Single Pulse
Single measurement
Low sample rate
Linear LiDAR
High power, low sensitivity

## Slide 45: Geiger-mode LiDAR
200MHz vs. 500 KHz
Technology Comparison
Large array collection
Collection from multiple angles
High sample rate (204 million samples per second)
Geiger LiDAR
Low Power, High Sensitivity (single photon)

## Slide 46: Benefits of Geiger-mode LiDAR Transportation Example
The results include ability to see finest detail from the desktop

## Slide 47: Questions?