## Slide 1: Infiltration
Introduction
Green Ampt method
Ponding time
Reading for today: Applied Hydrology sections 4.3 and 4.4
Reading for Tuesday: Applied Hydrology Sections 5.1 to 5.6

## Slide 2: Infiltration
depth
Wetting Zone
Transmission
Zone
Transition Zone
Saturation Zone
Wetting Front
q
General
  Process of water penetrating from ground into soil
  Factors affecting
    Condition of soil surface, vegetative cover, soil properties, hydraulic conductivity, antecedent soil moisture
  Four zones
    Saturated, transmission, wetting, and wetting front

## Slide 3: Infiltration
Infiltration rate, f(t)
  Rate at which water enters the soil at the surface (in/hr or cm/hr)
Cumulative infiltration, F(t)
  Accumulated depth of water infiltrating during given time period
t
f, F
F
f

## Slide 4: Infiltrometers
Single Ring
Double Ring
http://en.wikipedia.org/wiki/Infiltrometer

## Slide 5: Infiltration Methods
Horton and Phillips
  Infiltration models developed as approximate solutions of an exact theory (Richard’s Equation)
Green – Ampt
  Infiltration model developed from an approximate theory to an exact solution

## Slide 6: Green-Ampt Assumptions
Wetted Zone
Wetting Front
Ground Surface
Dry Soil
= increase in moisture content as wetting front passes
= Suction head at “sharp” wetting front
Conductivity, K
= Wetted depth
= Conductivity in wetted zone
Ponded Water
= Depth of water ponding on surface (small)

## Slide 7: Green-Ampt Soil Water Variables
Wetted Zone
Wetting Front
Ground Surface
Dry Soil
n = +
= initial moisture content of dry soil before infiltration happens
= increase in moisture content as wetting front passes
= moisture content (volume of water/total volume of soil)
= residual water content of very dry soil
= effective porosity
= porosity
n = + D

## Slide 8: Green-Ampt Parameters (Data from Table 4.3.1)
Texture | Porosity n | Residual Porosity ϴr | Effective Porosity ϴe | Suction Head ψ (cm) | Conductivity K (cm/hr)
Sand | 0.437 | 0.020 | 0.417 | 4.95 | 11.78
Loamy Sand | 0.437 | 0.036 | 0.401 | 6.13 | 2.99
Sandy Loam | 0.453 | 0.041 | 0.412 | 11.01 | 1.09
Loam | 0.463 | 0.029 | 0.434 | 8.89 | 0.34
Silt Loam | 0.501 | 0.015 | 0.486 | 16.68 | 0.65
Sandy Clay Loam | 0.398 | 0.068 | 0.330 | 21.85 | 0.15
Clay Loam | 0.464 | 0.155 | 0.309 | 20.88 | 0.10
Silty Clay Loam | 0.471 | 0.039 | 0.432 | 27.30 | 0.10
Sandy Clay | 0.430 | 0.109 | 0.321 | 23.90 | 0.06
Silty Clay | 0.470 | 0.047 | 0.423 | 29.22 | 0.05
Clay | 0.475 | 0.090 | 0.385 | 31.63 | 0.03

## Slide 9: Green-Ampt Porosity (Data from Table 4.3.1)
Chart: 
| Sand | Loamy Sand | Sandy Loam | Loam | Silt Loam | Sandy Clay Loam | Clay Loam | Silty Clay Loam | Sandy Clay | Silty Clay | Clay
Residual Porosity | 0.02 | 0.036 | 0.041 | 0.029 | 0.015 | 0.068 | 0.155 | 0.039 | 0.109 | 0.047 | 0.09
Effective Porosity | 0.417 | 0.401 | 0.412 | 0.434 | 0.486 | 0.33 | 0.309 | 0.432 | 0.321 | 0.423 | 0.385
0.09
0.45
0.03
Total porosity ~ 0.45
Clay soils retain water in ~ 20% of voids when dry
Other soils retain water in ~ 6% of voids when dry
ϴe
ϴr

## Slide 10: Conductivity and Suction Head (Data from Table 4.3.1)
Chart: 
| 4.95 | 6.13 | 11.01 | 8.89 | 16.68 | 21.85 | 20.88 | 27.3 | 23.9 | 29.22 | 31.63
Conductivity | 11.78 | 2.99 | 1.09 | 0.34 | 0.65 | 0.15 | 0.1 | 0.1 | 0.06 | 0.05 | 0.03
Suction Head, ψ (cm)
Conductivity, K
(cm/hr)
Sand
Clay
Silt Loam
Silty Clay Loam
Loamy Sand
Sandy Clay
Sandy Loam
Loam
Sandy Clay Loam
Clay Loam
Silty Clay

## Slide 11: Green – Ampt Infiltration
Wetted Zone
Wetting Front
Ponded Water
Ground Surface
Dry Soil

## Slide 12: Green – Ampt Infiltration (Cont.)
Apply finite difference to the derivative, between
  Ground surface
  Wetting front
Wetted Zone
Wetting Front
Ground Surface
Dry Soil

## Slide 13: Green – Ampt Infiltration (Cont.)
Nonlinear equation, requiring iterative solution
and integrate over time, gives
Use
t
f, F
F
f

## Slide 14: Initial Effective Saturation
Initial effective saturation 0 ≤ Se ≤ 1
Effective porosity

## Slide 15: Example
Determine the infiltration rate and the cumulative infiltration after 1 hour on a clay loam soil with initial effective saturation of 30%. Assume water is ponded instantaneously on the surface
Parameters:
Texture | Porosity n | Residual Porosity ϴr | Effective Porosity ϴe | Suction Head ψ (cm) | Conductivity K (cm/hr)
Clay Loam | 0.464 | 0.155 | 0.309 | 20.88 | 0.10

## Slide 16: Solution
Use Excel Goal Seek under “What If Analyis” in Data Tab

## Slide 17: Ponding time
Elapsed time between the time rainfall begins and the time water begins to pond on the soil surface (tp)

## Slide 18: Ponding Time
Up to the time of ponding, all rainfall has infiltrated (i = rainfall rate)
Potential
Infiltration
Actual Infiltration
Rainfall
Accumulated
Rainfall
Infiltration
Time
Time
Infiltration rate, f
Cumulative
Infiltration, F

## Slide 19: Example
Clay Loam soil, 30% effective saturation, rainfall 1 cm/hr intensity
What is the ponding time, and cumulative infiltration at ponding?
How long does it take to infiltrate 2 cm of water?
What is the infiltration rate at that time?

## Slide 20: Infiltration after ponding has occured
At ponding time, tp, the cumulative infiltration is equal to the amount of rainfall that has fallen up to that time, Fp = i*tp
After that time, the cumulative infiltration is given by
  )

## Slide 21: Solution