## Slide 1: Design Flows
Reading: Applied Hydrology, Sec 15-1 to 15-5

## Slide 2: Hydrologic design
For water control
  Mitigation of adverse effects of high flows or floods
  Design flows for conveyance structures (storm sewers, drainage channels) and regulation structures (detention basins, reservoirs)
For water use
  Management of water resources to meet human needs and conservation of natural life
  Determination of storage capacity

## Slide 3: Design flow computations
Methods
  Rational method
  Modified Rational Method
  SCS-TR55 Method

## Slide 4: Rational Method
Used to find peak flows for storm sewers
  If a rainfall of i intensity begins instantly and continues indefinitely, the rate of runoff will increase until the time of concentration (tc).
Assumptions
  Peak runoff rate at the outlet is a function of the average rainfall rate during tc (peak runoff does not result from a more intense storm of shorter duration during which only a portion of the watershed is contributing to the runoff)
  tc employed is the time for runoff to flow from the farthest point in the watershed to the inflow point of the sewer being designed
  Rainfall intensity is constant throughout the storm duration

## Slide 5: Rational Formula
The rational formula is given by:
Q = peak discharge in cfs which occurs at tc
i = rainfall intensity in in/hr (duration used to compute i = tc)
A = watershed area in acres
C = runoff coefficient (0 ≤C ≤ 1)
An urban area consisting of sub-areas with different surface characteristics
j = number of sub-catchments drained by a sewer
Composite rational equation

## Slide 6: Runoff Coefficient C
C is the most difficult variable to accurately determine in the rational method
The fraction of rainfall that will produce peak flow depends on:
  Impervious cover
  Slope
  Surface detention
  Interception
  Infiltration
  Antecedent moisture conditions

## Slide 7: C based on land use

## Slide 8: C values based on soil groups

## Slide 9: Rainfall intensity i
i: rainfall rate in in/hr
i is selected based on rainfall duration and return period
  duration is equal to the time of concentration, tc
  return period varies depending on design standards
tc = sum of inlet time (to) and flow time (tf) in the upstream sewers connected to the outlet
Li is the length of the ith pipe along the flow path and Vi is the flow velocity in the pipe.

## Slide 10: Pipe capacity for storm sewers
Assumption: pipe is flowing full under gravity
Manning or Darcy-Weisbach equation is applicable
Manning’s equation
Darcy-Weisbach equation
Valid for Q in cfs and D in feet. For SI units (Q in m3/s and D in m), replace 2.16 with 3.21.
Equation is valid for both SI and English system as long as the units are consistent

## Slide 11: Example 15.1.1
Given Td =10 min, C = 0.6, ground elevations at the pipe ends (498.43 and 495.55 ft), length = 450 ft, Manning n = 0.015, i=120T0.175/(Td + 27), compute flow, pipe diameter and flow time in the pipe

## Slide 12: Example with composite C
A
B
C
D
Reach | Description of flow | C | Slope (%) | Length (ft) | Area (acre)
A-B | Natural channel | 0.41 | 4.5 | 300 | 8
B-C | Natural channel | 0.85 | 3 | 540 | 20
C-D | Storm drain (n = 0.015, D = 3 ft) | 0.81 | 1.2 | 500 | 10
Compute tc and peak flow at D for i = 3.2 in/hr

## Slide 13: Solution
Compute tc for AB and BC using Kirpich formula in the text (Table 15.1.2)
For CD, compute velocity by Manning’s equation and tc = length/velocity

## Slide 14: Modified rational method
Extension of rational method for rainfalls lasting longer than the time of concentration
Can be used to develop hydrographs for storage design, rather than just flood peaks
Can be used for the preliminary design of detention storage for watersheds up to 20 or 30 acres

## Slide 15: Modified rational method equation
The hydrograph produced by modified rational method is a trapezoid with duration of rising and falling limb equal to tc.
Hydrograph for a basin with tc = 10 min and rainfall duration = 30 min will look like the following:
Td = 30 min
tc
tc
Q
t

## Slide 16: Application of modified rational method
Determine the critical duration (Td) and volume (Vs) for the design storm that will require maximum storage under future developed conditions
QA (cfs) is pre-development peak discharge, A is watershed area (acres), C is runoff coefficient, Tp = tc (min), and Td is in min
Qp is the future peak discharge associated with Td

## Slide 17: Ex. 15.4.1
Rainfall-intensity-duration equation is given as i=96.6/(Td+13.9), compute Td for a 25 acre watershed with C = 0.825. The allowable pre-development discharge is 18 cfs, and tc for pre- and post-development are 40 and 20 min, respectively.
A = 96.6, b = 13.9, QA = 18 cfs, Tp = 20 min, A = 25 acre, C = 0.825
Td = 27.23 min

## Slide 18: Ex. 15.4.2
Determine the maximum detention storage if g = 2
Detention storage is given by,
The volume of runoff after development = Qp*Td = 79, 140 ft3. Therefore, 53746/79140 = 68% of runoff will be stored in the proposed detention pond.

## Slide 19: Situational Awareness for Flash Flooding

## Slide 20: Emergency Response System (CAPCOG)

## Slide 21: ESInet – Emergency Services Internet Network
Slide from: John Brosowsky Product Development Director, GeoComm
Next Generation 911
Geographic location by coordinates

## Slide 22: Water Web Services Hub for CAPCOG
USGS
LCRA
NWS
COA
NDFD

## Slide 23: Tropical Storm Hermine, Sept 7-8, 2010

## Slide 24: Local Information during Tropical Storm Hermine (7-8 Sept 2010)
http://hydromet.lcra.org
http://coagis1.ci.austin.tx.us/website/COAViewer_fews/viewer.htm
http://ubcwcid.org/Overview/Overview.aspx?id=1
LCRA
City of Austin
Upper Brushy Creek (Round Rock)
TV

## Slide 25: Internet Communications
 | People | Media | Local Government | Federal Government
People |  |  |  | 
Media |  |  |  | 
Local Government |  |  |  | 
Federal Government |  |  |  | 
Information Consumers
Information Producers
We are all connected
Web services can play an important role in this……

## Slide 26
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060

## Slide 27: Colorado River at Austin
http://waterservices.usgs.gov/nwis/iv?sites=08158000&period=P7D&parameterCd=00060
I accessed this WaterML service at 7:10AM
And got back these flow data from USGS which are up to 6:00AM Central time

## Slide 29
World
United States
Texas
Austin
Home

## Slide 31: Observation Data Services
Provide real-time data services
  Streamflow, stage, precipitation
  Independent of WaterML version
Feed appropriate models with forcing data
  Land-surface models
  HMS, RAS

## Slide 32: River Channel Data Services
Convey inputs necessary for hydraulic models to run
  Connectivity, length, slope, N

## Slide 33: River Channel Data Services
http://explorer.arcgis.com/?open=ad7c4dbe299a458ca52b9caa725a2d4d

## Slide 34
IBM is collaborating with UT….
…. to help build a Smarter Planet

## Slide 36
Research Question: Can VLSI simulation models…..
….. be adapted to apply to river networks?

## Slide 37: Web Services HUB
USGS
LCRA
NWS
COA
NDFD
Web Services HUB
Inputs
Data
Services
(WaterML)
Mapping
Services
Models
Flood Mapping
Services
Maps
Outputs
Modeling
Services
Data and Mapping
Services
Data
Services
(WaterML)
Mapping
Services