## Slide 1: Upper Brushy Creek Water Control & Improvement District
Ruth Haberman, General Manager, UBCWCID
March 21, 2013

## Slide 2
DISTRICT OVERVIEW
Original District was formed by the Texas Legislature in 1956 for flood and erosion control within the Brushy Creek watershed
Primary focus has been operation and maintenance of 23 dams constructed by the SCS (now NRCS) in the 1950s and 1960s

## Slide 3
DAM MODERNIZATION
DAM 14
DAM 11
Since 2003, over $15M in tax revenue have been spent to modernize 21 dams.
Two dams remain to be modernized;
Dams 7 and 8.

## Slide 4
MISSION STATEMENT
The mission of the Upper Brushy Creek Water Control and Improvement District is to maintain and improve flood control structures and take appropriate measures to protect public safety as well as economic infrastructure of the District, in consultation and cooperation with other governmental entities. The District will actively foster a regional perspective and will encourage cooperation among governmental entities. We will accomplish these tasks utilizing cost-effective methods, minimizing the impact to the environment, considering the community values of our stakeholders, and conducting our business with openness, honesty and integrity.

## Slide 5: JURISDICTIONAL BOUNDARIES

## Slide 6
DRAINAGE AREAS

## Slide 7: MAJOR CHANGES IN THE COUNTY
 | 1960 | 1970 | 1980 | 1990 | 2000 | 2010 | 
Williamson County | 35,044 | 37,305 | 76,521 | 139,551 | 249,967 | 422,679 | 
http://www.census.gov/population/cencounts/tx190090.txt |  |  |  |  |  |  | 
http://www.txcip.org/tac/census/profile.php?FIPS=48491 |  |  |  |  |  |  | 
Chart: Williamson County, Texas
| 1960 | 1970 | 1980 | 1990 | 2000 | 2010
Williamson County | 35044 | 37305 | 76521 | 139551 | 249967 | 422679

## Slide 8
TS HERMINE FLOODING – September 8-9, 2010

## Slide 9
FLOODING ISSUES IN THE DISTRICT
Tropical Storm Hermine
District Infrastructure:
The dams functioned as designed, constructed and maintained.
The dams experienced only minor damage from the flooding.
The web-based Flood Monitoring System allowed District engineers, elected officials, and both City and County emergency managers to monitor the rainfall in the area.
Even with the dams operating as expected, there were still threats to public safety and risk of property damage.

## Slide 10
UPPER BRUSHY CREEK WATERSHED STUDY
Purpose:
Analyze watershed hydrology and hydraulics.
  Identify potential flood hazard areas.
Propose alternative solutions for regional flood hazard mitigation.
  Provide final report, models and documentation to all participants.
  Coordinate with FEMA and local government entities to incorporate study results into new regulatory FEMA Risk Maps (floodplain maps) for the entire watershed.

## Slide 11: Upper Brushy Creek Hydrologic Model
Jeff Irvin, URS

## Slide 12: Study Area

## Slide 13: Getting on Same Sheet of Music

## Slide 14: 449 Watersheds

## Slide 15: Hydrology: the Mindset
Hydrology = Data (Rainfall, Runoff, Land Use)
Data bad = Hydrology bad
Data good = Hydrology good
How do you test data?

## Slide 16: Hydrology: the Mindset
The data test:
Representative?
in place (where data taken)
in time period (same as application time period)
in amount of data?
Homogeneous? – applied on any data to be aggregated/ averaged
in place
in time
in collection method and accuracy

## Slide 17: Hydrology: the Mindset
The most representative and homogeneous data set is the best data set

## Slide 18: Hydrologic Model Calibration Data
Rainfall
  Sources of rainfall data?
  Which storms?
Runoff (flow or stage plus hydraulics)
  Sources?

## Slide 19: Choice of Calibration storms
The runoff hydrograph has two main parameters that define shape:
A parameter that defines how much rain runs off (runoff volume)
A parameter that defines time of peak (runoff temporal shape)

## Slide 20: Choice of Calibration Storms
Runoff volume (for a given rainfall) is a function of:

## Slide 21: Choice of Calibration Storms
Runoff volume (for a given rainfall) is a function of:
Rainfall
Land Use
Soil Type
% Impervious
Antecedent Runoff Condition

## Slide 22: Choice of Calibration Storms
What are data validity tests for a calibration storm used to calibrate a model rainfall/runoff relationship?
Rainfall

## Slide 23: Choice of Calibration Storms
What are data validity tests for a calibration storm for a model rainfall/runoff relationship?
Rainfall
  Representative
    In location and time
    In temporal shape
    In size
    Are there enough data?
      Spatially vs storm shape
      Temporally versus storm shape

## Slide 24: Upper Brushy WCID Dams

## Slide 25: Choice of Calibration Storms
    Representative in location and time?
    Are there enough data?
      Spatially vs storm shape

## Slide 26: Choice of Calibration Storms
    Are there enough data?
      Spatially vs storm shape

## Slide 27: Choice of Calibration Storms
    Are there enough data?
      Temporally versus storm shape

## Slide 28: Choice of Calibration Storms
    Representative?
      In temporal shape

## Slide 29: Choice of Calibration Storms

## Slide 30: Results of Rainfall/Runoff Calibration

## Slide 31: Why are results inconsistent?
Can we compare 2007 storm runoff results to 2012 storm runoff results?
Are the conditions that affect runoff homogeneous between the two storms?
Rainfall
Land Use
Soil Type
% Impervious
Antecedent Runoff Condition

## Slide 32: Antecedent Runoff
2007 Rainfall
2010 Rainfall
Are the two storms homogeneous in terms of antecedent conditions?

## Slide 33: Results of Rainfall/Runoff Calibration

## Slide 34: Results of Rainfall/Runoff Calibration

## Slide 35: Upper Brushy Creek Water Control and Improvement District
Dustin Mortensen, Freese and Nichols
March 21, 2013
Dam 7 Modernization
CE 374K Hydrology

## Slide 36: FNI OVERVIEW
Multi-service engineering, architecture and environmental science firm
118-year history
520+ employees across 14 offices throughout Texas
Client satisfaction is our top priority
We offer cost-effective solutions

## Slide 37: Dam 7 OVERVIEW
Intermediate Sized, High Hazard
Completed in 1965
Hydraulic Capacity - Passes 46% PMF
Drawdown Time (Auxiliary Spillway-Normal Pool)
Notes: Existing Dam stats:
  Intermediate Size
  Completed in 1965

## Slide 38: Normal Level

## Slide 39: Flood Level

## Slide 40: Flooded Park

## Slide 41: Spillway Hydraulics
Spillway discharge is calculated using weir equation
Where:
Q= discharge (cfs or m3/s)
C=Discharge coefficient
L=Length of the “lip” over which the water flows
H=Head above the weir

## Slide 42: Increase Capacity
Existing dam
Notes: The first question we need to answer is about capacity.
In the schematic design we looked at a range of options that included a, b, c
Schematic Design Concepts
  Meet dam safety Criteria (75% and 100% PMF)
  Incorporate the trail
  Consider regulatory floodplains
sent this slide.

## Slide 43: Increase H
Raising the dam
Notes: The first question we need to answer is about capacity.
In the schematic design we looked at a range of options that included a, b, c
Schematic Design Concepts
  Meet dam safety Criteria (75% and 100% PMF)
  Incorporate the trail
  Consider regulatory floodplains
sent this slide.

## Slide 44: Increase L
Widening the spillway

## Slide 45: Increase L and H
Range of options…

## Slide 46: Increase L

## Slide 47: Labyrinth Weir
Increases L without increases spillway footprint width
Dam 7 alternative has 1,800 feet of weir in 300 foot wide footprint
C is dependent on wall angles, wall height, head and crest shape

## Slide 48: Model Studies

## Slide 49: Model Studies

## Slide 50: Dam 7 Upstream

## Slide 51: Dam 7 Upstream

## Slide 52: Dam 7 Downstream

## Slide 53: Dam 7 Downstream

## Slide 54: Downstream
Wall Shape and Layout Options

## Slide 55: Labyrinth Weir Construction

## Slide 56: Platform Slab Construction

## Slide 57: Crest Shape

## Slide 58: Labyrinth Wall Construction

## Slide 59: Labyrinth Wall Construction

## Slide 60: Discussion / Q&A

## Slide 61: THANK YOU