## Slide 1: Geodesy, Map Projections and Coordinate Systems
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y,z) coordinate systems for map data

## Slide 2: Learning Objectives: By the end of this class you should be able to:
describe the role of geodesy as a basis for earth datums
list the basic types of map projection
identify the properties of common map projections
properly use the terminology of common coordinate systems
use spatial references in ArcMap so that geographic data is properly displayed
  determine the spatial reference system associated with a feature class or data frame
  use ArcGIS to convert between coordinate systems
calculate distances on a spherical earth and in a projected coordinate system

## Slide 3: Readings: Introduction
http://resources.arcgis.com/en/help/getting-started/articles/026n0000000s000000.htm

## Slide 4: Readings: Further Detail
http://resources.arcgis.com/en/help/main/10.2/#/What_are_map_projections/003r00000001000000/

## Slide 5: Revolution in Earth Measurement
Traditional Surveying uses benchmarks as reference points
Global Positioning uses fixed GPS receivers as reference points (Continuously Operating Reference System, CORS)
Some images and slides from Michael Dennis, National Geodetic Survey and Lewis Lapine, South Carolina Geodetic Survey

## Slide 6
(Press and hold)
Trimble GeoXHTM
Garmin GPSMAP 276C GPS Receiver
Global Position Systems

## Slide 7: GPS Satellites
Satellites are distributed among six offset orbital planes
24 satellites
6 orbital planes
12 hour return interval for each satellite
Notes: making two complete orbits in less than 24 hours

## Slide 8: How GPS works in five logical steps:
The basis of GPS is triangulation from satellites
GPS receiver measures distance from satellite using the travel time of radio signals
To measure travel time, GPS needs very accurate timing
Along with distance, you need to know exactly where the satellites are in space. Satellite location. High orbits and careful monitoring are the secret
You must correct for any delays the signal experiences as it travels through the atmosphere
Notes: Here's how GPS works in five logical steps:
1. The basis of GPS is "triangulation" from satellites.
2. To "triangulate," a GPS receiver measures distance using the travel time of radio signals.
3. To measure travel time, GPS needs very accurate timing which it achieves with some tricks.
4. Along with distance, you need to know exactly where the satellites are in space. High orbits and careful monitoring are the secret.
5. Finally you must correct for any delays the signal experiences as it travels through the atmosphere.

## Slide 9: Distance from satellite
Radio waves = speed of light
  Receivers have nanosecond accuracy (0.000000001 second)
All satellites transmit same signal “string” at same time
  Difference in time from satellite to time received gives distance from satellite
Notes: In a sense, the whole thing boils down to those "velocity times travel time" math problems we did in high school. Remember the old: "If a car goes 60 miles per hour for two hours, how far does it travel?"
Velocity (60 mph) x Time (2 hours) = Distance (120 miles)
In the case of GPS we're measuring a radio signal so the velocity is going to be the speed of light or roughly 186,000 miles per second.
The problem is measuring the travel time.

## Slide 10
Triangulation
Notes: Suppose we measure our distance from a satellite and find it to be 11,000 miles.
Knowing that we're 11,000 miles from a particular satellite narrows down all the possible locations we could be in the whole universe to the surface of a sphere that is centered on this satellite and has a radius of 11,000 miles.
Next, say we measure our distance to a second satellite and find out that it's 12,000 miles away.
That tells us that we're not only on the first sphere but we're also on a sphere that's 12,000 miles from the second satellite. Or in other words, we're somewhere on the circle where these two spheres intersect.

## Slide 11
Triangulation
Notes: If we then make a measurement from a third satellite and find that we're 13,000 miles from that one, that narrows our position down even further, to the two points where the 13,000 mile sphere cuts through the circle that's the intersection of the first two spheres.
So by ranging from three satellites we can narrow our position to just two points in space.
To decide which one is our true location we could make a fourth measurement. But usually one of the two points is a ridiculous answer (either too far from Earth or moving at an impossible velocity) and can be rejected without a measurement.
A fourth measurement does come in very handy for another reason however, but we'll tell you about that later

## Slide 12: Differential GPS
Differential GPS uses the time sequence of observed errors at fixed locations to adjust simultaneous measurements at mobile receivers
A location measurement accurate to 1 cm horizontally and 2cm vertically is now possible in 3 minutes with a mobile receiver
More accurate measurements if the instrument is left in place longer

## Slide 13: Tectonic Motions
From Sella et al., 2002
This has to take Tectonic Motions into account

## Slide 14: HORIZONTAL TECTONIC MOTIONS
Pacific Plate
North American Plate
Motion in cm/year
When is California not in North America …
…. when its on the Pacific Plate!

## Slide 15
{Latitude (f), Longitude (l), Elevation (z)}
Survey Benchmark
This leads to adjustments in locations of the national network of survey benchmarks

## Slide 17: Types of Coordinate Systems
(1) Global Cartesian coordinates (x,y,z) for the whole earth
(2) Geographic coordinates (f, l, z)
(3) Projected coordinates (x, y, z) on a local area of the earth’s surface
The z-coordinate in (1) and (3) is defined geometrically; in (2) the z-coordinate is defined gravitationally

## Slide 18: Global Cartesian Coordinates (x,y,z)
O
X
Z
Y
Greenwich
Meridian
Equator
•
Next 7 slides are from Dr Irmak

## Slide 19: Spatial Reference = Datum + Projection + Coordinate system
For consistent analysis the spatial reference of data sets should be the same.
ArcGIS does projection on the fly so can display data with different spatial references properly if they are properly specified.
ArcGIS terminology
  Define projection. Specify the projection for some data without changing the data.
  Project. Change the data from one projection to another.

## Slide 20: Geographic Coordinates (f, l, z)
Latitude (f) and Longitude (l) defined using an ellipsoid, an ellipse rotated about an axis
Elevation (z) defined using geoid, a surface of constant gravitational potential
Earth datums define standard values of the ellipsoid and geoid

## Slide 21: Shape of the Earth
We think of the
earth as a sphere
It is actually a spheroid, slightly larger in radius at the equator than at the poles

## Slide 22: Ellipse
P
F2
O
F1
a
b
X
Z


An ellipse is defined by:
Focal length = 
Distance (F1, P, F2) is
constant for all points
on ellipse
When  = 0, ellipse = circle
For the earth:
Major axis, a = 6378 km
Minor axis, b = 6357 km
Flattening ratio, f = (a-b)/a
~ 1/300

## Slide 23: Ellipsoid or Spheroid Rotate an ellipse around an axis
O
X
Z
Y
a
a
b
Rotational axis

## Slide 24: Standard Ellipsoids
Ref: Snyder, Map Projections, A working manual, USGS
Professional Paper 1395, p.12

## Slide 25: Geodetic Datums
World Geodetic System (WGS) – is a global system for defining latitude and longitude on earth independently of tectonic movement (military)
North American Datum (NAD) – is a system defined for locating fixed objects on the earth’s surface and includes tectonic movement (civilian)

## Slide 26: Horizontal Earth Datums
An earth datum is defined by an ellipse and an axis of rotation
NAD27 (North American Datum of 1927) uses the Clarke (1866) ellipsoid on a non geocentric axis of rotation
NAD83 (NAD,1983) uses the GRS80 ellipsoid on a geocentric axis of rotation
WGS84 (World Geodetic System of 1984) uses GRS80, almost the same as NAD83

## Slide 27: Adjustments of the NAD83 Datum
Slightly different (f, l) for benchmarks
Continuously Operating Reference System
Canadian Spatial Reference System
National Spatial Reference System
High Accuracy Reference Network

## Slide 28: Representations of the Earth
Earth surface
Ellipsoid
Sea surface
Geoid
Mean Sea Level is a surface of constant
gravitational potential called the Geoid

## Slide 29: THE GEOID AND TWO ELLIPSOIDS
GRS80-WGS84
(NAD83)
CLARKE 1866 (NAD27)
GEOID
Earth Mass
Center
Approximately
236 meters

## Slide 30: WGS 84 and NAD 83
International Terrestrial Reference Frame (ITRF) includes updates to WGS-84 (~ 2 cm)
North American Datum of 1983 (NAD 83) (Civilian Datum of US)
Earth Mass
Center
2.2 m (3-D)
dX,dY,dZ
GEOID
World Geodetic System of 1984 (WGS 84) is reference frame for Global Positioning Systems

## Slide 31: Definition of Latitude, f
(1) Take a point S on the surface of the ellipsoid and define there the tangent plane, mn
(2) Define the line pq through S and normal to the
tangent plane
(3) Angle pqr which this line makes with the equatorial
plane is the latitude f, of point S
O
f
S
m
n
q
p
r

## Slide 32: Cutting Plane of a Meridian
P
Meridian
Equator
plane
Prime Meridian

## Slide 33: Definition of Longitude, l
0°E, W
90°W
(-90 °)
180°E, W
90°E
(+90 °)
-120°
-30°
-60°
-150°
30°
-60°
120°
150°
l
l = the angle between a cutting plane on the prime meridian
and the cutting plane on the meridian through the point, P
P

## Slide 34: Latitude and Longitude on a Sphere
Meridian of longitude
Parallel of latitude


X
Y
Z
N
E
W

=0-90°S
P
O
R
=0-180°E
=0-90°N
•
Greenwich
meridian
=0°
•
Equator
=0°
•
•
=0-180°W
 - Geographic longitude
 - Geographic latitude
R - Mean earth radius
O - Geocenter

## Slide 35: Length on Meridians and Parallels
0 N
30 N
Df
Re
Re
R
R
A
B
C
Dl
(Lat, Long) = (f, l)
Length on a Meridian:
AB = Re Df
(same for all latitudes)
Length on a Parallel:
CD = R Dl = Re Dl Cos f
(varies with latitude)
D

## Slide 36
Example: What is the length of a 1º increment along
on a meridian and on a parallel at 30N, 90W?
Radius of the earth = 6370 km.
Solution:
A 1º angle has first to be converted to radians
p radians = 180 º, so 1º = p/180 = 3.1416/180 = 0.0175 radians
For the meridian, DL = Re Df = 6370 * 0.0175 = 111 km
For the parallel, DL = Re Dl Cos f
= 6370 * 0.0175 * Cos 30
= 96.5 km
Parallels converge as poles are approached

## Slide 37: Curved Earth Distance (from A to B)
Shortest distance is along a “Great Circle”
A “Great Circle” is the intersection of a sphere with a plane going through its center.
1. Spherical coordinates converted to Cartesian coordinates.
2. Vector dot product used to calculate angle  from latitude and longitude
3. Great circle distance is R, where R=6378.137 km2
X
Z
Y
•

A
B
Ref: Meyer, T.H. (2010), Introduction to Geometrical and Physical Geodesy, ESRI Press, Redlands, p. 108

## Slide 38: Three systems for measuring elevation
Orthometric heights
(land surveys, geoid)
Ellipsoidal heights
(lidar, GPS)
Tidal heights
(Sea water level)
Conversion among these height systems has some uncertainty

## Slide 39: Trends in Tide Levels (coastal flood risk is changing)
Charleston, SC
+ 1.08 ft/century
- 4.16 ft/century
+ 2.13 ft/century
Juneau, AK
Galveston, TX
1900
2000
1900
2000
1900
2000

## Slide 40: Geoid and Ellipsoid
Ocean
Geoid
Earth surface
Ellipsoid
Gravity Anomaly
Gravity anomaly is the elevation difference between
a standard shape of the earth (ellipsoid) and a surface
of constant gravitational potential (geoid)

## Slide 41: Definition of Elevation
Elevation Z
•
P
z = zp
z = 0
Mean Sea level = Geoid
Land Surface
Elevation is measured from the Geoid

## Slide 42
Gravity Recovery and Climate Experiment (GRACE)
NASA Mission launched in 2002
Designed to measure gravity anomaly of the earth
Two satellites, 220 km apart, one leading, one trailing
Distance between them measured by microwave to 2µm
High gravity force pulls satellites together
Lower gravity force, lets them fly apart more
Gravity anomaly = difference from average
http://earthobservatory.nasa.gov/Features/GRACE/

## Slide 43: Gravity Recovery and Climate Experiment (GRACE) Force of gravity responds to changes in water volume Water is really heavy! Gravity is varying in time and space.
Gravity Anomaly of Texas, 2002 – 2012
Normal
In 2011, we lost 100 Km3 of water or 3 Lake Mead’s

## Slide 44: GRACE and Texas Reservoir Water Storage
Surface Water Reservoirs
In 2011 we lost 9 Km3 of water from reservoirs
Grace Satellites
Surface water reservoir storage is closely correlated with the GRACE data
In 2011 we lost 100 Km3 of water overall
Normal
Normal

## Slide 45: Vertical Earth Datums
A vertical datum defines elevation, z
NGVD29 (National Geodetic Vertical Datum of 1929)
NAVD88 (North American Vertical Datum of 1988)
takes into account a map of gravity anomalies between the ellipsoid and the geoid

## Slide 46: Converting Vertical Datums
Corps program Corpscon (not in ArcInfo)
  http://crunch.tec.army.mil/software/corpscon/corpscon.html
Point file attributed with the elevation difference between NGVD 29 and NAVD 88
NGVD 29 terrain + adjustment
= NAVD 88 terrain elevation

## Slide 47: Importance of geodetic datums NAVD88 – NGVD29 (cm)
NAVD88 higher in West
NGVD29 higher in East
Orthometric datum height shifts are significant relative to BFE accuracy, so standardization on NAVD88 is justified
More than 1 meter difference

## Slide 48: Geodesy and Map Projections
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data

## Slide 49: Earth to Globe to Map
Representative Fraction
Globe distance Earth distance
=
Map Scale:
Map Projection:
Scale Factor
Map distance Globe distance
=
(e.g. 1:24,000)
(e.g. 0.9996)

## Slide 50: Geographic and Projected Coordinates
(f, l)
(x, y)
Map Projection

## Slide 51: Types of Projections
Conic (Albers Equal Area, Lambert Conformal Conic) - good for East-West land areas
Cylindrical (Transverse Mercator) - good for North-South land areas
Azimuthal (Lambert Azimuthal Equal Area) - good for global views

## Slide 52: Conic Projections (Albers, Lambert)

## Slide 53: Cylindrical Projections (Mercator)
Transverse
Oblique

## Slide 54: Azimuthal (Lambert)

## Slide 55: Albers Equal Area Conic Projection

## Slide 56: Lambert Conformal Conic Projection

## Slide 57: Universal Transverse Mercator Projection

## Slide 58: Lambert Azimuthal Equal Area Projection

## Slide 59: Web Mercator Projection (used for ESRI Basemaps)
The spatial reference for the ArcGIS Online / Google Maps / Bing Maps tiling scheme is WGS 1984 Web Mercator (Auxiliary Sphere).
Web Mercator is one of the most popular coordinate systems used in web applications because it fits the entire globe into a square area that can be covered by 256 by 256 pixel tiles.

## Slide 60
Central Meridian
Standard Parallel
(0,0)
(20037, 19971 km)
= earth rad * Π
6378 km
6357 km
Earth radius
Web Mercator Parameters

## Slide 61: Projections Preserve Some Earth Properties
Area - correct earth surface area (Albers Equal Area) important for mass balances
Shape - local angles are shown correctly (Lambert Conformal Conic)
Direction - all directions are shown correctly relative to the center (Lambert Azimuthal Equal Area)
Distance - preserved along particular lines
Some projections preserve two properties

## Slide 62: Projection and Datum
Two datasets can differ in both the projection and the datum, so it is important to know both for every dataset.

## Slide 63: Geodesy and Map Projections
Geodesy - the shape of the earth and definition of earth datums
Map Projection - the transformation of a curved earth to a flat map
Coordinate systems - (x,y) coordinate systems for map data

## Slide 64: Coordinate Systems
Universal Transverse Mercator (UTM) - a global system developed by the US Military Services
State Plane Coordinate System - civilian system for defining legal boundaries
Texas Centric Mapping System - a statewide coordinate system for Texas

## Slide 65: Coordinate System
(fo,lo)
(xo,yo)
X
Y
Origin
A planar coordinate system is defined by a pair
of orthogonal (x,y) axes drawn through an origin

## Slide 66: Universal Transverse Mercator
Uses the Transverse Mercator projection
Each zone has a Central Meridian (lo), zones are 6° wide, and go from pole to pole
60 zones cover the earth from East to West
Reference Latitude (fo), is the equator
(Xshift, Yshift) = (xo,yo) = (500000, 0) in the Northern Hemisphere, units are meters

## Slide 67: UTM Zone 14
Equator
-120°
-90 °
-60 °
-102°
-96°
-99°
Origin
6°

## Slide 68: State Plane Coordinate System
Defined for each State in the United States
East-West States (e.g. Texas) use Lambert Conformal Conic, North-South States (e.g. California) use Transverse Mercator
Texas has five zones (North, North Central, Central, South Central, South) to give accurate representation
Greatest accuracy for local measurements

## Slide 69: ArcGIS Spatial Reference Frames
Defined for a feature dataset in ArcCatalog
XY Coordinate System
  Projected
  Geographic
Z Coordinate system
Domain, resolution and tolerance

## Slide 70: Horizontal Coordinate Systems
Geographic coordinates (decimal degrees)
Projected coordinates (length units, ft or meters)

## Slide 71: Vertical Coordinate Systems
None for 2D data
Necessary for 3D data

## Slide 72: ArcGIS .prj files

## Slide 73: Summary Concepts
The spatial reference of a dataset comprises datum, projection and coordinate system.
For consistent analysis the spatial reference of data sets should be the same.
ArcGIS does projection on the fly so can display data with different spatial references properly if they are properly specified.
ArcGIS terminology
  Define projection. Specify the projection for some data without changing the data.
  Project. Change the data from one projection to another.

## Slide 74: Summary Concepts (Cont.)
Two basic locational systems: geometric or Cartesian (x, y, z) and geographic or gravitational (f, l, z)
Mean sea level surface or geoid is approximated by an ellipsoid to define an earth datum which gives (f, l) and distance above geoid gives (z)

## Slide 75: Summary Concepts (Cont.)
To prepare a map, the earth is first reduced to a globe and then projected onto a flat surface
Three basic types of map projections: conic, cylindrical and azimuthal
A particular projection is defined by a datum, a projection type and a set of projection parameters

## Slide 76: Summary Concepts (Cont.)
Standard coordinate systems use particular projections over zones of the earth’s surface
Types of standard coordinate systems: UTM, State Plane
Web Mercator coordinate system (WGS84 datum) is standard for ArcGIS basemaps